## Slide 1: Reduced Network Model Development for Fluidized Bed Biomass Gasification: Capturing Gas Bypassing and Devolatilizing Particle Segregation with CFD
Addison K. Stark, Richard B. Bates, Christos Altantzis, Ahmed F. Ghoniem
Reacting Gas Dynamics Laboratory, Department of Mechanical Engineering, MIT.
NETL Workshop on Multi-Phase Flow, August 5th – 6th , 2014

## Slide 2: Brief Overview and Background
Biomass as a Feedstock-
Reactor Network Modeling of Reactive FBBG
The Current CFD Study-
NETL Workshop on Multi-Phase Flow, August 5-6, 2014

## Slide 3: The Importance of Predictive Pyrolysis Chemistry in Fluidized Bed Gasifier Modeling
Stoichiometric pyrolysis
Competing Pathways
Competing Pathways for Cellulose, Hemicellulose & Lignin
Milne, T.A. et al. NREL/TP-570-25357 1998.
Tar Yields and Dew Points
[Yang et al., 2008]
Wood
Vol + Char
[Shafizadeh and Chin, 1977]
Number of species, computational intensity, Stiffness
[Koufopanos et al, 1989]

## Slide 4: Multi-Scale Chemistry Modeling of Fluidized Bed Biomass Gasification
Gas-Phase modeling
  State of the art mechanism:
    Ranzi et al.
    400+ species
    16K+ reactions
Solids Phase Modeling
  Heat transfer dependence
  Lagrangian in nature

## Slide 5: Reactor Network Model (RNM) Formulation

## Slide 6: Impact of bubble-phase on gas-phase conversion.
Devol.
Gases
Air
Freeboard
(PFR)
Bubble
(PFR)
Emulsion
(CSTR)
x
1-x
Chart: Methane
| 973 | 1003 | 1033 | 1063 | 1093 | 1123 | 1153 | 1183 | 1213 | 1243 | 1273
x=1 | 0.037452 | 0.038152 | 0.038785 | 0.039343 | 0.039591 | 0.039282 | 0.038322 | 0.036824 | 0.035077 | 0.033362 | 0.031789
x=.75 | 0.03747 | 0.038108 | 0.038674 | 0.039155 | 0.039359 | 0.039068 | 0.038197 | 0.036846 | 0.035264 | 0.033679 | 0.032175
x=.5 | 0.037145 | 0.037697 | 0.038171 | 0.038569 | 0.038729 | 0.038484 | 0.037756 | 0.036615 | 0.035245 | 0.033821 | 0.032405
x=.25 | 0.036317 | 0.036733 | 0.037104 | 0.037444 | 0.03762 | 0.037494 | 0.036995 | 0.036144 | 0.035043 | 0.033808 | 0.03248
x=0 | 0.034222 | 0.034467 | 0.034766 | 0.035171 | 0.035539 | 0.035718 | 0.035612 | 0.035128 | 0.034309 | 0.03326 | 0.035196
van Paasen & Kiel (Beech) | 0.0422 | 0.04225 | 0.040066
van Paasen & Kiel (Willow) | 0.03567 | 0.04176 | 0.04806 | 0.04312 | 0.0468
Narvaez (1996) | 0.039875 | 0.039238 | 0.037472 | 0.034523 | 0.030311 | 0.034902 | 0.02943 | 0.032034
Chart: CO
| 973 | 1003 | 1033 | 1063 | 1093 | 1123 | 1153 | 1183 | 1213 | 1243 | 1273
x=1 | 0.20395 | 0.20136 | 0.19901 | 0.19706 | 0.19552 | 0.1944 | 0.1933 | 0.19159 | 0.18893 | 0.18561 | 0.18247
x=.75 | 0.2048 | 0.20248 | 0.20029 | 0.19833 | 0.19664 | 0.19512 | 0.19336 | 0.19087 | 0.18755 | 0.18392 | 0.1809
x=.5 | 0.20637 | 0.20441 | 0.20261 | 0.20094 | 0.19938 | 0.19778 | 0.19573 | 0.19281 | 0.18902 | 0.18496 | 0.18159
x=.25 | 0.20889 | 0.20726 | 0.20584 | 0.20442 | 0.20288 | 0.20109 | 0.19869 | 0.19535 | 0.19117 | 0.18675 | 0.18301
x=0 | 0.21414 | 0.21291 | 0.21183 | 0.21056 | 0.20885 | 0.20671 | 0.20393 | 0.20022 | 0.19563 | 0.19098 | 0.18656
van Paasen & Kiel (Beech) | 0.14095 | 0.14196 | 0.14633
van Paasen & Kiel (Willow) | 0.13485 | 0.14268 | 0.16643 | 0.154
 | 0.12408 | 0.15221 | 0.156 | 0.15726 | 0.17006 | 0.17428 | 0.16531
Chart: Hydrogen
| 973 | 1003 | 1033 | 1063 | 1093 | 1123 | 1153 | 1183 | 1213 | 1243 | 1273
x=1 | 0.052919 | 0.05848 | 0.064441 | 0.070621 | 0.077235 | 0.084699 | 0.09325 | 0.10274 | 0.11246 | 0.12146 | 0.12901
x=.75 | 0.051401 | 0.056748 | 0.062646 | 0.069018 | 0.076098 | 0.084203 | 0.093416 | 0.10344 | 0.1135 | 0.12263 | 0.1301
x=.5 | 0.04921 | 0.054264 | 0.059994 | 0.066354 | 0.073579 | 0.081896 | 0.091297 | 0.10145 | 0.11166 | 0.1211 | 0.12903
x=.25 | 0.40338 | 0.40187 | 0.40023 | 0.3986 | 0.39688 | 0.39503 | 0.39315 | 0.39137 | 0.38979 | 0.38841 | 0.3872
x=0 | 0.04385 | 0.04829 | 0.053702 | 0.059923 | 0.067072 | 0.075273 | 0.084472 | 0.094581 | 0.10522 | 0.11554 | 0.12583
van Paasen & Kiel (Beech) | 0.07174 | 0.07098 | 0.097552
van Paasen & Kiel (Willow) | 0.04698 | 0.06264 | 0.08188 | 0.06512 | 0.0963
Narvaez (1996) | 0.044958 | 0.074436 | 0.077689 | 0.084877 | 0.08998 | 0.09698 | 0.10046 | 0.10342
Chart: Total Tar
| 973 | 1003 | 1033 | 1063 | 1093 | 1123 | 1153 | 1183 | 1213 | 1243 | 1273
1 | 13940.2274 | 10997.3405 | 8455.1622 | 6856.2978 | 5476.8851 | 4275.3754 | 3421.3267 | 2934.6288 | 2776.0109 | 2886.8528 | 3212.8884
0.75 | 13979.9661 | 11096.752 | 8715.1966 | 7173.2757 | 5791.7136 | 4572.776 | 3700.7064 | 3195.8326 | 3014.0081 | 3093.3775 | 3377.5714
0.5 | 14425.9855 | 11542.2401 | 9235.9542 | 7748.8656 | 6345.0728 | 5062.2316 | 4112.7153 | 3531.1891 | 3272.536 | 3275.1047 | 3484.0608
0.25 | 15142.3872 | 12321.777 | 10070.8504 | 8652.2255 | 7201.4167 | 5800.091 | 4693.7337 | 3950.5516 | 3550.7533 | 3439.556 | 3558.5595
0 | 16263.5112 | 13532.8901 | 11277.9718 | 9896.8618 | 8373.2163 | 6788.9366 | 5432.9139 | 4434.0033 | 3816.9984 | 3474.1596 | 4810.7209
van Paasen & Kiel (Beech) | 10000 | 7600 | 8100
Narvaez (1996) | 18763.146 | 9035.612 | 13395.702 | 9981.08 | 8502.892 | 4947.987 | 3715.752 | 2815.272 | 2812.868 | 2101.963
Kurkela and Stahlberg | 18004.784 | 11594.743 | 9450.702 | 6310.444 | 3976.322
~40% difference

## Slide 7: Impact of bubble-phase on gas-phase conversion.
Devol.
Gases
Air
Freeboard
(PFR)
Bubble
(PFR)
Emulsion
(CSTR)
x
1-x
How can we calculate x?
Exist a number of correlations…
Davidson (1963)
Babu et al. (1978)
Johnsson et al. (1991)
Would like to verify with CFD.
Chart: Predicted Bubble Fraction
| 1.0528904607346301 | 2.1889038525798798 | 3.32491724442513 | 4.4609306362703904 | 5.5969440281156402 | 6.7329574199608899 | 7.8689708118061503 | 9.0049842036514001 | 10.1409975954967 | 11.2770109873419 | 12.413024379187201 | 13.549037771032401 | 14.6850511628777 | 15.8210645547229 | 16.957077946568202 | 18.093091338413402 | 19.229104730258701 | 20.365118122103901 | 21.501131513949201 | 22.637144905794401
Babu | 0.018763 | 0.15978 | 0.23778 | 0.29499 | 0.34034 | 0.37782 | 0.40965 | 0.43722 | 0.46145 | 0.48299 | 0.50233 | 0.51982 | 0.53576 | 0.55037 | 0.56381 | 0.57625 | 0.5878 | 0.59857 | 0.60863 | 0.61807
Davidson | 0.0069468 | 0.073745 | 0.11472 | 0.14578 | 0.17094 | 0.19211 | 0.21039 | 0.22646 | 0.24081 | 0.25376 | 0.26557 | 0.27641 | 0.28643 | 0.29574 | 0.30445 | 0.31261 | 0.32029 | 0.32755 | 0.33443 | 0.34096
Johnsson | 0.0023938 | 0.051179 | 0.095415 | 0.13571 | 0.17257 | 0.20641 | 0.23759 | 0.26642 | 0.29315 | 0.31799 | 0.34115 | 0.36279 | 0.38305 | 0.40206 | 0.41994 | 0.43678 | 0.45267 | 0.46768 | 0.4819 | 0.49537

## Slide 8: Validation Study, reactive 3D simulation: van Paasen & Kiel, 2004
diameter
0.074 m
Reactor height 1.1 m
Static bed
height
0.149 m
Simulation parameters | 
Quantity | Value
Reactor height, m | 1.1
Reactor diameter, m | 0.074
Gas density, kg/m3 | Variable
Gas viscosity, kg/(m s) | Variable
Solid phase 1 | Pine wood
Solid phase 1 particle diameter, mm | 1
Solid Phase 1 particle density, kg/m3 | 650
Solid Phase 1 feedrate, kg/hr | .10,.14,.28,.5, .75, 1, 1.5
Inert solid phase | Silica sand
Inert particle diameter, mm | 0.27
Inert particle density, kg/m3 | 2100
Superficial gas velocity, m/s | .039,.052,.10,.19, .285, 0.38, .57
Initial bed height, m | 0.2
Pressure, atm | 1
Inflow gas temperature. K | 1073
Initial inert material temperature. K | 1073
Biomass import temperature, K | 300
Devolatilization Chemistry | Competing pathway Shrinking Core
Wood
Gas
Tar
Char
(Shafizadeh, 1982)

## Slide 9: Simulation parameters – van Paasen & Kiel 2004, air blown FBBG
Simulation parameters | 
Quantity | Value
Reactor height, m | 1.1
Reactor diameter, m | 0.074
Gas density, kg/m3 | Variable
Gas viscosity, kg/(m s) | Variable
Solid phase 1 | Pine wood
Solid phase 1 particle diameter, mm | 1
Solid Phase 1 particle density, kg/m3 | 650
Solid Phase 1 feedrate, kg/hr | .10,.14,.28,.5, .75, 1, 1.5
Inert solid phase | Silica sand
Inert particle diameter, mm | 0.27
Inert particle density, kg/m3 | 2100
Superficial gas velocity, m/s | .039,.052,.10,.19, .285, 0.38, .57
Initial bed height, m | 0.2
Pressure, atm | 1
Inflow gas temperature. K | 1073
Initial inert material temperature. K | 1073
Biomass import temperature, K | 300
Devolatilization Chemistry | Competing pathway Shrinking Core

## Slide 10: Devolatilization Modeling
Devolatilization dynamics are strongly influenced by particle radius.
Shrinking Core Model Implemented for Eulerian Modeling Framework:
Trade-off of devolatilization time and mixing time important for well-stirred assumption.

## Slide 11: Data Analysis and Visualization
θ
y
r
Cylindrical coordinates (Bakshi et al.)
For 2D visualization hemispheres averaged.

## Slide 12: Results
NETL Workshop on Multi-Phase Flow, August 5-6, 2014
Mixing of biomass and char in reacting bed-

## Slide 13: Time Averaged Solids Distributions
Biomass Concentration
Voidage and Gas Velocity

## Slide 14: Bubble-Phase vs Emulsion Phase
Time averaged data is used to analyze pseudo-steady state operation.
  Average bed height
  Average voidage
  Reaction zones
Velocity normalized voidage is used to calculate bubble bypassing fraction
  Gives the effective voidage experienced by gaseous flow through the bed.

## Slide 15: Dependence of gas distribution on inlet velocity
Chart: Bed Expansion
| 1.0528904607346301 | 2.1889038525798798 | 3.32491724442513 | 4.4609306362703904 | 5.5969440281156402 | 6.7329574199608899 | 7.8689708118061503 | 9.0049842036514001 | 10.1409975954967 | 11.2770109873419 | 12.413024379187201 | 13.549037771032401 | 14.6850511628777 | 15.8210645547229 | 16.957077946568202 | 18.093091338413402 | 19.229104730258701 | 20.365118122103901 | 21.501131513949201 | 22.637144905794401
Babu | 1.0191 | 1.1902 | 1.312 | 1.4184 | 1.5159 | 1.6072 | 1.6939 | 1.7769 | 1.8568 | 1.9342 | 2.0094 | 2.0826 | 2.1541 | 2.224 | 2.2926 | 2.3599 | 2.426 | 2.4911 | 2.5552 | 2.6183
Davidson | 1.007 | 1.0796 | 1.1296 | 1.1707 | 1.2062 | 1.2378 | 1.2664 | 1.2928 | 1.3172 | 1.3401 | 1.3616 | 1.382 | 1.4014 | 1.4199 | 1.4377 | 1.4548 | 1.4712 | 1.4871 | 1.5025 | 1.5174
Johnsson | 1.0108 | 1.1251 | 1.208 | 1.2796 | 1.3441 | 1.4035 | 1.4592 | 1.5118 | 1.5618 | 1.6096 | 1.6556 | 1.6999 | 1.7427 | 1.7843 | 1.8247 | 1.8639 | 1.9023 | 1.9397 | 1.9762 | 2.012
Current Results | 1.1291 | 1.1946 | 1.3694 | 1.6464 | 1.952 | 2.2258 | 2.7825
Chart: Bubble Fraction (1-x)
| 1.0528904607346301 | 2.1889038525798798 | 3.32491724442513 | 4.4609306362703904 | 5.5969440281156402 | 6.7329574199608899 | 7.8689708118061503 | 9.0049842036514001 | 10.1409975954967 | 11.2770109873419 | 12.413024379187201 | 13.549037771032401 | 14.6850511628777 | 15.8210645547229 | 16.957077946568202 | 18.093091338413402 | 19.229104730258701 | 20.365118122103901 | 21.501131513949201 | 22.637144905794401
Babu | 0.018763 | 0.15978 | 0.23778 | 0.29499 | 0.34034 | 0.37782 | 0.40965 | 0.43722 | 0.46145 | 0.48299 | 0.50233 | 0.51982 | 0.53576 | 0.55037 | 0.56381 | 0.57625 | 0.5878 | 0.59857 | 0.60863 | 0.61807
Davidson | 0.0069468 | 0.073745 | 0.11472 | 0.14578 | 0.17094 | 0.19211 | 0.21039 | 0.22646 | 0.24081 | 0.25376 | 0.26557 | 0.27641 | 0.28643 | 0.29574 | 0.30445 | 0.31261 | 0.32029 | 0.32755 | 0.33443 | 0.34096
Johnsson | 0.0023938 | 0.051179 | 0.095415 | 0.13571 | 0.17257 | 0.20641 | 0.23759 | 0.26642 | 0.29315 | 0.31799 | 0.34115 | 0.36279 | 0.38305 | 0.40206 | 0.41994 | 0.43678 | 0.45267 | 0.46768 | 0.4819 | 0.49537
Current Results | 0.15091 | 0.20236 | 0.35727 | 0.49655 | 0.60909 | 0.668 | 0.74018

## Slide 16: Conclusion and Summary
NETL Workshop on Multi-Phase Flow, August 5-6, 2014
Summary of outcomes-
Implications for modeling and reactor design-
Next steps-

## Slide 17: Summary and Implications for Modeling
Summary of work
Conclusions
A 3D reactive CFD study was conducted to test the main assumption of the Davidson two-phase theory and related correlations:
  All gas in excess of minimum fluidization velocity is in the bubble phase.
Devolatilization chemistry with a shrinking core model was employed
  Allows for study of impact of particle diameter on mixing timescales as well as devolatilization timescales
Influence of fluidization rate on chemical phenomena was investigated.
Davidson TPT and Johnsson Models Under-predict Gas bypassing at high slugging flow-rates
  Babu Captures overall trend, however. Easily implemented without CFD.
A large amount of bubble bypassing is observed.
  As the reactor approaches slugging, do not achieve well mixed zone until high in the freeboard
Lab-scale studies which utilize saw dust (<=1mm particles) are far from representing realistic fluidized bed reactors
  Timescale of devolatilization is too fast.
    Devolatilizing particles are not well distributed.

## Slide 18: Other Observations and Next Steps
At high flow-rates with large amounts of bubble bypassing mixing is poor in the bed.
  Therefore Davidson model is incomplete to describe full reactor.
Devol.
Gases
Air
Freeboard
(PFR)
Bubble
(PFR)
Emulsion
(CSTR)
x
1-x
Devol.
Gases
Air
Freeboard
(PFR)
Bubble
(PFR)
Emulsion
(CSTR)
z
1-z
y
1-y

## Slide 19: References and Acknowledgements
Bakshi, A., C. Altantzis, and A. F. Ghoniem. "Towards Accurate Three-Dimensional Simulation of Dense Multi-Phase Flows Using Cylindrical Coordinates." Powder Technology, 2014, 264, 242-255.
Davidson, J. “The two-phase theory of fluidization: successes and opportunities.” AIChE Symposium Series, 1991, 87, 1-12.
Koufopanos, C. A. et al. “Modelling of the pyrolysis of biomass particles. Studies on kinetics, thermal and heat transfer effects.” The Canadian Journal of Chemical Engineering, 1991, 69, 907-915.
Milne, T., et al. “Biomass gasifier tars: Their nature, formation and conversion.” National Energy Technology Laboratory (NETL), 1998.
Shafizadeh, F. “Introduction to Pyrolysis of Biomass.” Journal of Analytical and Applied Pyrolysis, 1982, 3, 283-305.
van Paasen, S. V. B. & Kiel, J. H. A. “Tar formation in a fluidised bed gasifier.” Energy Research Center of the Netherlands, 2004.
Yang, Y. B.et l. “Combustion of a Single Particle of Biomass.” Energy & Fuels, 2008, 22, 306-316.
This work was generously funded by BP