## Slide 1: A New Drag Law for the Accurate Prediction of the Pressure Drop in a Bubbling Fluidized Bed
O. O. Ayenia, C.L. Wua,b, J. B. Joshic, K. Nandakumara*
aCain Department of Chemical Engineering, Louisiana State University, Baton Rouge 70803, U.S.A.
bANSYS Inc, 15915 Katy Fwy, Houston 77094, U.S.A.
cHomi Bhabha National Institute, Training School Complex, Anushaktinagar, Mumbai – 400 094

## Slide 2: Objective
To validate an in-house computational code against the NETL-SSCP Experimental results
To attempt to “improve the reliability of computational modeling of multiphase flows”
Outline
Present Governing equations
Show disparity between our initial computational effort and the NETL-SSCP experiments
Present an alternative drag law

## Slide 3
Governing Equations (DEM-CFD)

## Slide 4: Drag Correlations
Wen & Yu
Gidaspow (Hybrid of Wen & Yu and Ergun)
is volume fraction of gas
is a constitutive drag source term
where is drag coefficient
Particle diameter

## Slide 5: Soft Sphere Model
– spring constant
– Friction factor
– Damping constant
E – Young’s modulus
– Poisson ratio
Mindlin, R. D. and H. Deresiewicz (1953). "Elastic spheres in contact under varying oblique forces." Transactions of the ASME-Series E 20: 327-344.

## Slide 6: Material Properties
Particle Properties(Nylon Beads) | 
 | 3256
 | 1131
Normal Restitution coeff. | 0.84
Friction Coefficient | 0.35
 | 95,356
 | 1.09m/s
 | 11m/s
Fluid Properties(Air) | 
 | 1.03
 | 1.8E-05
P-V coupling | SIMPLE
 | 1948
Particle Properties(Nylon Beads) | 
Normal Restitution coeff. | 0.84
Friction Coefficient | 0.35
 | 95,356
 | 1.09m/s
 | 11m/s
Fluid Properties(Air) | 
P-V coupling | SIMPLE
 | 1948

## Slide 7: Test Facility
Test Section
Plenum

## Slide 8: Geometry, Boundary Conditions, Numerics
Pressure Outlet
Impenetrable, No-slip Walls(4)
Uniform Velocity Inlet
0.23m
1.22m
0.075m
Cell Count |  | 16 × 80 × 5 | 
Cell Size |  | 0.014375×0.015×0.015375m3 | 
 |  | 0.001s | 
 |  | 2E-5s | 
Numerics |  |  | 
Momentum discretization |  |  | 3rd order MUSCL
P-V coupling |  |  | SIMPLE
Cases |  |  | 
1 | Inlet velocity |  | 
2 | Inlet velocity |  | 
3 | Inlet velocity |  | 
Cell Count |  | 16 × 80 × 5 | 
Cell Size |  | 0.014375×0.015×0.015375m3 | 
 |  | 0.001s | 
 |  | 2E-5s | 
Numerics |  |  | 
Momentum discretization |  |  | 3rd order MUSCL
P-V coupling |  |  | SIMPLE
Cases |  |  | 
1 | Inlet velocity |  | 
2 | Inlet velocity |  | 
3 | Inlet velocity |  | 
Notes: Monotone Upstream-Centered Schemes for Conservation Laws

## Slide 9: Animations

## Slide 10: Flow Features
Non-Uniform flow patterns due to:
  Non-linear drag
  Non-ideal particle collisions
Intense Bubbling and Slugging

## Slide 11: Time-Averaged Vertical Velocity
Samples taken at 0.076m from the distributor

## Slide 12: RMS Vertical Velocity
Samples taken at 0.076m from the distributor

## Slide 13: Pressure Drop
TIME-AVERAGED PRESSURE DROP ACROSS BED (Taps at 0.0413m and 0.3461)

## Slide 14: New Drag Law
Pandit and Joshi (1998) Present the derivation for drag experienced by a particle in fixed and expanded beds under uniform fluidization
  Energy balances employed,
    - Energy input rate, - Potential energy at top of bed, - Net dissipation in bulk of bed
  Use force balance to find expression for in terms of , the net dissipation per unit mass of fluid
  Turbulence intensity,
Account for additional energy head to generate bubbles
Pandit, A. and J. Joshi (1998). "Pressure drop in fixed, expanded and fluidized beds, packed columns and static mixers-A unified approach." Reviews in Chemical Engineering 14(4-5): 321-371.

## Slide 15: New Drag Law
Where
As ,
(fixed bed)
=1.75
is volume fraction of gas
is volume fraction of solids
is Minimum fluidization velocity
is Superficial gas velocity
Bed height at incipient fluidization
is Dynamic Bed Height

## Slide 16: Notes
Bed is turbulent providing justification for using the turbulent drag term alone
Bed is not fixed, hence use of Ergun equation in its original form suspect
Drag is modified in two ways
  By allowing to become applicable to expanded beds
  Including additional energy dissipation into bubbles that appears as the factor

## Slide 17: Time-Averaged Vertical Velocity
Taps at 0.076m from the distributor

## Slide 18: Pressure Drop
TIME-AVERAGED PRESSURE DROP ACROSS BED (Taps at 0.0413m and 0.3461)

## Slide 19: Conclusions
Shown the inadequacy of conventional drag laws in bubbling fluidized beds
Energy required in creating bubbles has been taken into account
A new drag law based on energy and force balances proposed
Necessary to make modifications for transition from laminar to turbulent for generality

## Slide 20: Acknowledgements