## Slide 1
Mehrdad Shahnam1, Aytekin Gel1,2, Arun K. Subramaniyan3, Jordan Musser1, Jean F. Dietiker1,4
1Department of Energy, National Energy Technology Laboratory
2Alpemi Consulting, 3GE Global Research, 4WVURC
Bayesian Calibration of Reaction Rate Model Parameters in Reacting Multiphase Flow Simulations for Advanced Coal Gasifier Technology Development
NETL Multiphase Flow Sciences Workshop
August 12-13, 2015 Morgantown, WV

## Slide 2: Uncertainty Quantification
Motivation
  There is a strong need to assess the credibility of numerical prediction results for wider acceptance in development of new technologies for fossil fuel based clean energy.
  Verification, Validation and Uncertainty Quantification (VV&UQ) methods provide the required objective means in establishing the confidence level from simulation outcome.
Objective
  Determine the best set of methods, techniques and software tools applicable for reactive multiphase flow simulation in order to assess the uncertainty in simulation results

## Slide 3: The Need for Advanced Clean Energy Technologies for Fossil Fuels
Over 40% of electricity worldwide is generated through the use of coal
New environmental regulations, mandating reduction on green house gases and other pollutants will impact coal-based power plants
Coal gasification technology promises to generate power with reduced environmental impact
Department of Energy’s National Energy Technology Laboratory (NETL) has launched an R&D program to quantify uncertainty in model predictions for reacting gas-solids systems, such as a gasifier
The goal is to develop a practical framework to quantify the various types of uncertainties and assess the impact of their propagation in the computer models of the physical system

## Slide 4: Approach
Non-intrusive UQ approach is selected in order to treat the the validated scientific simulation software as a black box without the need for structural changes.
Surrogate models of the quantities of interest (QoI) are created through sampling techniques and UQ analysis with Bayesian methodology is employed.
UQ analysis performed:
  Forward propagation of input uncertainties to their effect on QoI,
  Global sensitivity analysis,
  Bayesian calibration.

## Slide 5: Transient Fluidized Bed Gasifier Simulation
(1)Shayan Karimipour, Regan Gerspacher, Rajender Gupta, Raymond J. Spiteri, “Study of factors affecting syngas quality and their interactions in fluidized bed gasification of lignite coal”, Fuel, Vol. 103, January 2013, Pages 308-320, ISSN 0016-2361, http://dx.doi.org/10.1016/j.fuel.2012.06.052.
Schematic diagram of the lab-scale fluidized-bed gasifier used for experiments1
Coal inlet
Outlet
Air inlet
Uncertainty Quantification Study Properties:
Input parameters with Uncertainty [range] Coal Flow Rate (g/s) : [0.036 – 0.063] (2) Particle Size (mm) : [70 – 500] (3) H2O / O2 ratio : [0.5 – 1.0]
Quantities of Interest: Carbon Conversion (%) H2/CO CH4/H2 Species mole fractions at exit

## Slide 6: Transient Fluidized Bed Gasifier Simulation
Transient CFD simulations performed with MFIX-TFM (https://mfix.netl.doe.gov )
Coal pyrolysis, combustion, steam & CO2 gasification along with H2, CO and CH4 oxidation are modeled using 11 chemical reactions.
Total of 33 transport equations are simultaneously solved for transport of 21 species and three phases (gas, coal and sand).
Computational cost per sampling simulation:
  2D : 2~3 weeks on 16 cores
  3D (30x350x30) : 7~8 weeks on 96 cores

## Slide 7: Animation of Voidage and CO Mass Fraction (2D slice of a 3D simulation)
Voidage Mass Fraction of CO

## Slide 8: Surrogate Model
Surrogate models for H2 and CO mole fraction, based on 30 samples of CFD runs and three uncertain input parameters.
Surrogate model for H2 mole fraction
Surrogate model for CO mole fraction
Particle size (µm)
Particle size (µm)
H2O/O2
H2O/O2
Coal flow rate (gr/s)
Coal flow rate (gr/s)

## Slide 9: Parity Plot of H2 Mole Fraction Surrogate Model Prediction, with Uncertainty vs. Experiment
Prediction of
the emulator constructed from both simulation & experiments
Gaussian process model based model discrepancy
Points on the line indicates perfect comparison between measured data and simulation results
Experimental Data = Simulation Results + Discrepancy

## Slide 10: Parity Plot of H2 Mole Fraction Surrogate Model Prediction, with Uncertainty, Corrected for Model Discrepancy vs. Experiment
Model discrepancy corrected emulator prediction of # 4
Experimental Data = Simulation Results + Discrepancy

## Slide 11: Parity Plot of H2 Mole Fraction Surrogate Model Prediction, with Uncertainty vs. Experiment
Hydrogen mole fraction is under-predicted across the entire parametric space
Surrogate model prediction, with uncertainty interval

## Slide 12: Parity Plot of H2 Mole Fraction Surrogate Model Prediction, with Uncertainty, Corrected for Model Discrepancy vs. Experiment
Model discrepancy corrected prediction values of hydrogen mole fraction and their uncertainty intervals across the entire parameter space

## Slide 13: Parity Plot of H2 Mole Fraction Surrogate Model Prediction, with Uncertainty, Corrected for Model Discrepancy vs. Experiment
Prediction by the surrogate model (green)
Prediction by the surrogate model, corrected for the discrepancy (blue)

## Slide 14: Global Sensitivity Analysis
A lab scale fluidized bed gasifier is operating under the following conditions:
  Coal flow rate = 0.049 gr/s
  Coal particle diameter = 285 µm
  Steam to oxygen ratio = 0.75
Question: How sensitive simulation results are to changes in
  Gasification reaction model
  Water gas shift reaction model
  CO oxidation reaction model
  Char oxidation reaction model
  Bed temperature

## Slide 15: Global Sensitivity Analysis
Percent variability in CO, H2 and CO2 mole fraction due to changes in bed temperature and reaction models for water gas shift, gasification, CO oxidation and char oxidation.

## Slide 16: Surrogate Models Can Provide Insight in Trends
Variation in CO Mole Fraction due to Variation in Bed Temperature and Gasification Rate Constant
  Top right: catalytic water gas shift reaction
  Bottom right: non-catalytic water gas shift reaction
CO Mole Fraction values obtained by using catalytic water gas shift reaction is closer to the measured values (0.12 to 0.14)

## Slide 17: Surrogate Models Can Provide Insight in Trends
Variation in H2 Mole Fraction due to Variation in Bed Temperature and Gasification Rate Constant
  Top right: catalytic water gas shift reaction
  Bottom right: non-catalytic water gas shift reaction
H2 Mole Fraction values obtained by using catalytic water gas shift reaction is closer to the measured values (0.12 to 0.15)

## Slide 18: Bayesian Calibration
Posterior distribution for the multiplier to the gasification kinetics model (PCCL Calibration factor) obtained via Bayesian Calibration, when prior distribution was assumed to vary between [0.09 & 0.55]
MFIX Simulation Results before & after Bayesian Calibration for CO mole fraction

## Slide 19: Bayesian Calibration
Posterior distribution for all five calibration parameters (PCCL Calibration factor, reaction models and bed temperature) obtained via Bayesian Calibration.
Bayesian Calibration Suggests the Following Parameter Settings:
PCCL = 0.398
Bed Temp. = 1070.5 K
WGS model = 1
Coal Comb. Model = 2
CO Oxid. Model = 1 or 2

## Slide 20: Conclusions
Uncertainty Quantification analysis provided uncertainty intervals for the CFD simulation results in the parametric space tested.
Sensitivity Analysis points to the water gas shift reaction as being the most important reaction in effecting the syngas composition (CO and H2)
Based on analysis of the surrogate models for CO and H2, the catalytic water gas shift reaction is the suitable reaction to use for conversion of CO to H2.
Bayesian Calibration provided a better assessment on one of the most uncertain model parameter, i.e., gasification rate constant and improvement in CFD results was demonstrated.
Sensitivity analysis shows that improvements in the catalytic water gas shift reaction model, gasification reaction model and heat transfer between gas and solid phases can lead to improvement in model prediction

## Slide 21: Computational Resources
Computational resources provided by:
  The supercomputer facility at DOE-NETL
  The ALCC program at the National Energy Research Scientific Computing Center (NERSC), a DOE Office of Science User Facility supported by the Office of Science of the U.S. Department of Energy under Contract No. DE-AC02-05CH11231.