## Slide 1: Modeling and validation of coal combustion in a circulating fluidized bed using Eulerian-Lagrangian approach
U.S. Department of Energy, National Energy Technology Laboratory (NETL)
2015 Workshop on Multiphase Flow Science
August 12, 2014
Allan Runstedtler, Haining Gao, Patrick Boisvert

## Slide 2: Multiphase Reacting Flows
CanmetENERGY high pressure entrained flow gasifier/combustor
U. S. Steel Canada blast furnace – coal and natural gas injection

## Slide 3: Fluid Bed Combustion
Improve efficiency and cost of CCS by 20+% compared to conventional PC boilers with 98% capture
Oxy-Pressurized Fluid Bed Combustion (Oxy-PFBC)
  < 30% electricity cost increase
  High efficiency
  Fuel flexibility
  Power and steam
  Low water consumption
Pressurized Chemical Looping Combustion (PCLC)
  Shale gas, fuel gas and asphaltene, coke
  High efficiency
  H2, power and steam
  Flexible operating pressure

## Slide 4: Model Validation: Pilot Plant – “Minibed”
CanmetENERGY
Dual Fluid Bed System for CaL, CLC, oxy-fuel
Specifications
Calciner / Oxy-Combustor:
T < 1050 °C
P – atmospheric
ID = 0.1 m
H = 5.0 m
Vf < 6.0 m/s
Fuel type: solid fuels
Fuel feed rate < 10 kg/h
Oxygen stream = 99.9%
Carbonator / Air Reactor:
T < 1050 °C
P – atmospheric
ID = 0.1 m
H = 3.0 m
Vf < 2.0 m/s
Solid transfer < 50 kg/h

## Slide 5: Circulating Fluid Bed – “Minibed”
Feed inlet

## Slide 6: Modeling approach: Eulerian-Lagrangian
Pros:
Straightforward to include particle size distribution
Straightforward to setup heterogeneous reactions
Cons:
Longer calculation time
Restrictions on computational grid
More challenging to achieve numerical stability
Treat particles as particle parcels
Drag force model: Gidaspow
Particle interactions are modeled using granular model
- Granular Viscosity: Gidaspow
- Granular Bulk Viscosity: Lun et al.
- Packing limit: 0.6
With respect to Eulerian-Eulerian calculation:

## Slide 7: Geometry and Mesh

## Slide 8: Highvale Coal Combustion
Air combustion
Oxy-fuel combustion
CO2 volume percent
O2 volume percent
Time
11:40
12:14

## Slide 9: Boundary Conditions, Properties
Input gas: air
Velocity: 3.96 m/s
(31.97 kg/hr)
Temperature:800°C (after sintered plate)
0.5m
Sand weight: 5.5 kg
Sand particle density: 3300 kg/m3
Sand size distribution:
Olivine sand 32B4:35-70=2:1
1180.0μm | 0.0055
1015.0μm | 0.0275
725.0μm | 0.1765
512.5μm | 0.3947
362.5μm | 0.1714
256.0μm | 0.1689
181.0μm | 0.0388
128.0μm | 0.0083
53.0μm | 0.0083
>0.9

## Slide 10: Fuel Inlet
Coal feed rate: 6.69 kg/hr
Air rate: 1.54 kg/hr
Temperature (air & coal): 18°C
Coal injection velocity: 0.1 m/s,
normal to surface
Coal particle density: 1069 kg/m3
Coal specific heat: 1530 J/(kg·K)
Size (mm) | wt %
0.15 | 10
0.3 | 26.5
0.85 | 46.5
2.36 | 13.9
5.35 | 3.1
Coal size input:
Proximate analysis | 
Moisture | 16.8
Ash | 22.8
Volatile | 24.5
Fixed carbon | 35.9
Ultimate analysis | 
Carbon | 44.01
Hydrogen | 2.85
Nitrogen | 0.67
Oxygen (diff) | 12.87
Highvale analysis data:

## Slide 11: Recycle Inlet—Gases
O2, % | 1.65
CO2, % | 15.58
CO, ppm | 90.99
Return leg gas rate: 1.29 kg/s
Temperature: 604°C
Gas compositions:
SO2 and NO not included, the balance gas is nitrogen

## Slide 12: Recycle inlet Determine recycle sand rate per size group
Particle density: 3300 kg/m3
Temperature: 604°C
Particle injection velocity: 0.1 m/s, normal
Recycled sand based on simulation results of sand particles escaping at the outlet:
Particles larger than 700 µm neglected because relatively small fraction leaving outlet
Particles smaller than 128 µm not recycled (not captured by the cyclone)—also a small fraction
Particle size, μm | mass rate, kg/hr
512.5 | 15.5
362.5 | 83.3
256.0 | 103.6
181.0 | 25.5
Total | 227.9

## Slide 13
Total coal particle escape rate: 4.32 kg/hr at 42.25 s flow time
 | density, kg/m3 | char mass fraction | Volatile mass fraction | Mass fraction
0.15mm | 312 | 0.0861 | 0.00 | 0.0330
0.3mm | 465 | 0.3871 | 0.00 | 0.1141
0.85mm | 608 | 0.5311 | 0.00 | 0.8221
2.36mm | 168 | 0.0750 | 0.00 | 0.0309
No particles larger than 5.30 mm in diameter escaped the minibed at 42.25 s flow time
Only include 0.3 mm and 0.85 mm coal particles in recycled material
>0.93
Recycle inlet Determine recycle coal rate per size group

## Slide 14: Wall Heat Flux
Heat flux (out): 3296 W/m2
(Calculated assuming 800oC inner wall temperature and 75oC outer wall temperature)
Heat flux (out): 271 kW/m2
(Heat flux to account for the energy from mini
bed to heat air from 57oC to 800oC)

## Slide 15: Coal Reactions
Coal Reaction Data | 
Devol A | 200000
Devol E (J/kmol) | 4.9884e7
Char A | 0.002
Char E (J/kmol) | 7.9e7
Heterogeneous reactions:
Coal → volatile
Char + O2 → CO
Gas-phase reactions:
Volatile +O2 → CO + H2O
CO + O2 → CO2
Constant diameter model

## Slide 16: Results: Sand Fluidization
Start-up

## Slide 17: Results: Sand Fluidization
Sand volume fraction at 52.2 s flow time

## Slide 18
Pressure drop
Predicted: 1500-3000 Pa
Measured: 2500-3600 Pa
Pressure boundary condition: 0 Pa

## Slide 19
Measured: 800-8010C
Predicted: 912-9420C
Measured: 787-7940C
Predicted: 767-8270C
Measured: 820-8280C
Predicted: 955-10010C
Temp. oC

## Slide 20
Measured: 1.3-1.8%
Predicted: 1.7-4.2%
O2 mole fraction

## Slide 21
Measured: 15%
Predicted: 13-16%
CO2 mole fraction

## Slide 22
CO mole fraction
Measured: 55-155 ppm
Predicted: 0 ppm

## Slide 23
Coal particles residence time at 50 s flow time
150um
300um
850um
2.36mm
5.35mm

## Slide 24
1
2
3
Coal particle burnout at 52 s flow time
300um
850um
5.35mm
2.36mm
150um

## Slide 25
Summary
The modeling approach has demonstrated its capacity to predict complicated fluidized bed coal combustion operation.
Various input conditions need further verification such as size distributions for coal and sand, and coal reaction data.
Different drag laws, particle interaction models need further investigation.
The simulation time is very long.

## Slide 26
Multiphase Flows
Enbridge oil transmission pipeline
Sediment deposition and under-deposit corrosion
Notes: ASTM G184-06. Standard Practice for Evaluating and Qualifying Oil Field and Refinery Corrosion Inhibitors Using Rotating Cage
ASTM G202-12. Standard Test Method for Using Atmospheric Pressure Rotating Cage
ASTM G170-01a. Standard Guide for Evaluating and Qualifying Oilfield and Refinery Corrosion Inhibitors in the Laboratory