## Slide 1
Liqiang Lu (NETL ORISE)
Kisoo Yoo (NETL ORISE)
Sofiane Benyahia (NETL)
Coarse grained particle method for simulation of liquid-solids reacting flow
MFIX-DEM
MFIX-CGP
Rare Earth Elements leaching from coal-byproducts
Vitamins
of modern industry
Waste

## Slide 2
Outlines
1. Physical model of coarse grained particle method (CGPM)
2. Computation speed of CGPM Vs. MP-PIC
3. Simulation of a bubbling fluidized bed
4. Simulation of a counter-current fluidized leaching bed
5. Summary

## Slide 3
Physical model of CGPM: general introduction
Particle number
Improved Speed
Solid flow = 18.4kg/h
Residence Time=80s
Simulate 400 s, using 100 cores with 100% efficiency.
Time needed ~ 3.65 YEARs!
16
particles
MP-PIC ( W=8 )
Coarse grained
particle method
CGPM (W=8)
Guaranteed Accuracy
Collision force is NOT calculated
Collision force is calculated!
Kazari, M., Roko, K., Kawaguchi, T., Tanaka, T.a.T., Y.,, 1995. A Study on Conditions for Similarity of Particle Motion in Numerical Simulation of Dense Gas-Solid Two Phase Flow.
Benyahia, S., Galvin, J.E., 2010. Estimation of Numerical Errors Related to Some Basic Assumptions in Discrete Particle Methods. Industrial & Engineering Chemistry Research 49, 10588-10605.
Lu, L., Xu, J., Ge, W., Yue, Y., Liu, X., Li, J., 2014. EMMS-based discrete particle method (EMMS–DPM) for simulation of gas–solid flows. Chemical Engineering Science 120, 67-87.
Not NEW, Need verification in Liquid-Solids Reacting flow
Computationally
infeasible for real systems!
To capture particle-scale chemical reactions
Euler-Lagrangian method
Small time steps
Huge number of particles
Non-physically overlapped, pass through
Particle Number = 6.4 x106
Time steps = 1.0x10-6S
Solved by lumping several real particles into a parcel
Time steps

## Slide 4
CGPM
Physical model of CGPM: our implementation of CGPM in MFIX
The drag force is same for each real particle within a CGP
[1] Benyahia, S., Galvin, J.E., 2010. Estimation of Numerical Errors Related to Some Basic Assumptions in Discrete Particle Methods. Industrial & Engineering Chemistry Research 49, 10588-10605.
[2] Lu, L., Xu, J., Ge, W., Yue, Y., Liu, X., Li, J., 2014. EMMS-based discrete particle method (EMMS–DPM) for simulation of gas–solid flows. Chemical Engineering Science 120, 67-87.
[3] G. G. JOSEPH, R. ZENIT, M. L. HUNT and A. M. ROSENWINKEL (2001). Particle–wall collisions in a viscous fluid. Journal of Fluid Mechanics, 433, pp 329-346
Well accepted
Newly added
The species concentration is same for each real particle within a CGP
The chemical reaction is same for each real particle within a CGP
Little physical basis, strong assumptions,
Need further investigation
The collision force is calculated by DEM using a collision diameter of dCGP = dpW1/3
The spring constant is same to that used in traditional CFD-DEM simulation
The restitution coefficient is smaller to keep a same energy dissipation[1,2] (in gas-solids flow)
or taking into the effect of hydrodynamic lubrication[3] (in liquid-solids flow)
Other properties (like friction) are same to original particles
/W
Same Fdrag
Same kchem
DEM

## Slide 5
Fluid phase continuity: | 
Fluid phase momentum: | 
Interphase momentum transport: | 
Species transport: | 
Constitute equations: | 
Physical model of CGPM: Governing equations, implemented in MFIX, with hybrid parallel
Fluid phase equations
Solid phase equations
Compromise between accuracy and speed
Different system has different maximum W
With more accurate interpolation method, Larger W can be used
The only parameter in this model is: statistic weight W
W
1 100 200 ……
DEM
?
Speed
Accuracy

## Slide 6
Outlines
1. Physical model of coarse grained particle method (CGPM)
2. Computation speed of CGPM Vs. MP-PIC
3. Simulation of a bubbling fluidized bed
4. Simulation of a counter-current fluidized leaching bed
5. Summary

## Slide 7
Computation speed of CGPM VS MP-PIC
 | MP-PIC | CGPM
dt.CFD | Varied, stabilized at 1.0 x 10-3 | Varied, stabilized at 1.0 x 10-3
dt.Solid | Varied, stabilized at 1.0 x 10-3 | Fixed at 1.0 x 10-4

## Slide 8
For simple flow, they gave very similar results.
Using 16 CPU cores on a single host with openMP multi-threads
MP-PIC is only about 10%-20% faster than CGPM
The speed priority of MP-PIC is not that much as supposed although time step is 10 times larger.
For 10.24 million computation particles is about 0.58 physical seconds per hour
The corresponding total strong scale efficiency of 256 processes is about 40%
This offers us an opportunity to investigate pilot or even industrial reactors with particle scale models
Computation speed of CGPM Vs. MP-PIC

## Slide 9
Outlines
1. Physical model of coarse grained particle method (CGPM)
2. Computation speed of CGPM Vs. MP-PIC
3. Simulation of a bubbling fluidized bed
4. Simulation of a counter-current fluidized leaching bed
5. Summary

## Slide 10
Bubbling fluidized bed: chemical reaction rate
Yoo, K.; Lu, L.; Benyahia, S., Modeling and simulation of rare earth element extraction by ion exchange reaction in batch reactor. submitted to Journal of Hydrometeorology.

## Slide 11
Bubbling fluidized bed: : physical properties and hydrodynamic results
Experiment:
dp1 = 0.045~0.060 cm
dp2 = 0.060~0.900 cm
dp = 0.045cm, with W=1000(left) and W=500(right)

## Slide 12
Bubbling fluidized bed: similar chemical reaction results
Xiao, Y.-f., Chen, Y.-y., Feng, Z.-y., Huang, X.-w., Huang, L., Long, Z.-q., Cui, D.-l., 2015. Leaching characteristics of ion-adsorption type rare earths ore with magnesium sulfate. Transactions of Nonferrous Metals Society of China 25, 3784-3790
The simulation result compares well with experimental data
The result is insensitive to statistic weight
The system can be treated as monodisperse and corresponding diameter is 0.45 mm and 0.9 mm.

## Slide 13
Outlines
1. Physical model of coarse grained particle method (CGPM)
2. Computation speed of CGPM Vs. MP-PIC
3. Simulation of a bubbling fluidized bed
4. Simulation of a counter-current fluidized leaching bed
5. Summary

## Slide 14
Counter-current fluidized bed: geometry and operating conditions
Valve open
Valve closed
Simulated with point source
Simulated with pressure drop in porous medium
Varied operating condition & reactor geometry
Residence time & inlet position
Leachate recycling
Decreasing the L:S ratio
Increasing REE
concentrations

## Slide 15
Counter-current fluidized bed case Base: Solid movement
Liquid inlet
Solid inlet
Base
SIH58
L36
L36S36
W20

## Slide 16
Counter-current fluidized bed case Base : solid distribution
There is a dense phase near the liquid inlet and above the dense phase is the dilute phase
The REE mass fraction gradient is well established in both dilute region and dense region

## Slide 17
Counter-current fluidized bed : Reactant recycle & L:S ratio
REE mass fraction at top outlet and bottom outlet with different liquid recycle fraction
REE mass fraction with reduced liquid-solids ratio
Lu, L., Yoo, K., Benyahia, S., 2016. Coarse grained particle method for simulation of liquid-solids reacting flows. Submitted to I&ECR

## Slide 18
Counter-current fluidized bed : residence time & inlet position
REE mass fraction with increased residence time and elevated solids inlet position
REE leaching fraction variation with increased residence time and solid inlet position
Lu, L., Yoo, K., Benyahia, S., 2016. Coarse grained particle method for simulation of liquid-solids reacting flows. Submitted to I&ECR

## Slide 19
Outlines
1. Physical model of coarse grained particle method (CGPM)
2. Computation speed of CGPM Vs. MP-PIC
3. Simulation of a bubbling fluidized bed
4. Simulation of a counter-current fluidized leaching bed
5. Summary

## Slide 20
Summary
Varied Process Conditions
MFIX-CGPM
  Thousands of Seconds Simulation
  Optimize
  Chemical Reactors
  Potential to Include CFD in Process Simulator

## Slide 21
A1. Physical model of CGPM: recent researches in this area
1 | Sakai, M.; Koshizuka, S., Large-scale discrete element modeling in pneumatic conveying. Chem. Eng. Sci. 2009, 64, (3), 533-539. | Binary collision due to all the original particles included in the coarse grain particle occurs when the binary collision of the coarse particle i and j is occurred.
2 | Benyahia, S.; Galvin, J. E., Estimation of Numerical Errors Related to Some Basic Assumptions in Discrete Particle Methods. Ind. Eng. Chem. Res. 2010, 49, (21), 10588-10605. | To account for the extra dissipation due to the increased number of collisions, a modification to the restitution coefficient is proposed.
3 | Hilton, J. E.; Cleary, P. W., Comparison of non-cohesive resolved and coarse grain DEM models for gas flow through particle beds. Appl. Math. Model. 2014, 38, (17–18), 4197-4214. | The directions of the normal forces for all the fine grain particle contacts are parallel and aligned There are no strong pressure gradients within a coarse grain particle. Gas velocity is constant across the coarse grain particle.
4 | Lu, L.; Xu, J.; Ge, W.; Yue, Y.; Liu, X.; Li, J., EMMS-based discrete particle method (EMMS–DPM) for simulation of gas–solid flows. Chem. Eng. Sci. 2014, 120, (0), 67-87. | 

## Slide 22
A2: GPU Accelerated on-line interactive simulation (work from other group)
On a personal laptop (45k parcels @ 1 GPU)
On a GPU cluster (200k parcels @ 12 GPUs)
Ge, W. et al. 2015. Multiscale discrete supercomputing - a game changer for process simulation? Chemical Engineering & Technology 38, 575-584.
Lu, L. et al. 2016. Computer virtual experiment on fluidized beds using a coarse-grained discrete particle method. Chemical Engineering Science (http://www.sciencedirect.com/science/article/pii/S0009250916304353)

## Slide 23
A3: Counter-current fluidized bed case Base: stable operation
The particles are added into the reactor from time 0 s and reach a stable state after about 80 s.
At the beginning, the flow rate at both top outlet and bottom outlet are constant and summed up equals the inlet rate 20 g/s.
After around 80 s, a little fluctuation is also observed due to the outflow of particles.
total = top outlet + bot outlet
Inlet = 20 g/s

## Slide 24
A4: Counter-current fluidized bed case Base: product quality
In the simulation, 20% of the total outlet liquid is mixed with original liquid and recycled into the reactor.
There is a great change at first 200 s and at about 800 s the REE mass fraction at outlet reaches 0.028% and stabilized.
Because of recycled liquid, the REE leaching fraction at outlet is reduced from 80% to 75% at first 200 s and then stabilized

## Slide 25
A5: Verification of CGPM: improved result with more precise interpolation schemes
Increase the influence area of coarse grained particles!
W = 1, 8, 27 with DPVM