## Slide 1
MFIX-DEM Enhancement towards Industrially-Relevant Flows
Workshop on Multiphase Flow Science
August 10 2016
Peiyuan Liu
Dept. of Chemical Engineering
University of Colorado Boulder
Project leads:
Dr. Ray Cocco (PSRI, co-PI)
Dr. Ray Grout (NREL, co-PI)
Prof. Thomas Hauser (Univ. CO, co-PI)
Prof. Christine Hrenya (Univ. CO, PI)
Funding by the U.S. Department of Energy under Grant No. DE-FE0026298

## Slide 2: Team
University of Colorado
Chemical & Biological Engineering
DEM modeling of granular and gas-solid flows, MFIX
University of Colorado
Research Computing
High-performance computing, CFD
NREL
Computational Science
High-performance computing, CFD
PSRI
Industrial Application and Experiments of Particle Flows
Prof. Christine Hrenya
Dr. William Fullmer
Dr. Peiyuan Liu
Prof. Thomas Hauser
Tim Brown
Dr. Ray Grout
Dr. Hari Sitaraman
Dr. Allan Issangya
Dr. Ray Cocco
Dr. Deepthi
Vaidhynathan
Aaron Holt
Notes: Our team is formed by a collaboration of engineering and computation scientists. Professor Christine Hrenya from CU is leading the team with expertise in DEM and multiphase flow modelling. Professor Thomas Hauser, who is the director of research computing at CU and Dr Ray Grout at NREL are leading the computational experts. Dr. Ray Cocco from PRSI will be help us with industrially relevant experiments.

## Slide 3: Motivation
van der Hoef et al, Annu. Rev. Fluid Mech 2008
TFM
DEM-CFD
DNS
Less CPU time
More detail, fewer closures
Experiments
DEM-CFD
?
Np ~ 104 - 106
Np ~ 1010
  Motivation:
  DEM application toward industrially relevant systems
Notes: The motivation of this project is to extend the current MFIX-DEM towards industrially relevant flows. As shown on the left, compared with TFM and DNS, DEM is gaining popularity as it has the advantage of less closures and more tractable computational time. However, simulation industrially problems with DEM is still a challenge. As shown on the right, lab-scale experiment of a fluidized is commonly containing 4~6 order of magnitude more particles than state-of-art DEM can handle. When drawing to scale, the DEM geometry disappears, questioning the predictions obtained from the simulations.

## Slide 4: Outline
Objective: MFIX-DEM toward industrially relevant problems
Industrial Survey
Define Benchmark Cases
Profiling Benchmark Cases
Preliminary Results
Notes: Here is outline of the progress we made to approach our goal. First we conducted industrial survey to understand their needs. Next we defined representative benchmark cases and performed profiling to understand the current capability of the MFIX-DEM. Finally we will show some preliminary results where we can demonstrate the enhanced performance via our modifications of the code.

## Slide 5: Understanding Industry Needs: Survey by PSRI
DEM usage
Sectors distribution of 18 respondents
Expected value added through DEM
Software packages
Percentage
Notes: First, we talk about the industrial survey, which covers a wide of distribution of industrial sectors as shown on the left. In terms of DEM usage, 67% are using CFD and DEM and most of them are using commercial packages. And They are all very optimistic about DEM and over 80% would expect DEM to provide valuable information for their industry.

## Slide 6: Understanding Industry Needs: Survey by PSRI
Acceptable turnover time
No. of companies
Cocco, R., Fullmer, W.D., Liu, P., Hrenya, C.M., CFD-DEM: Modeling the small to understand the large (submitted). Chem. Eng. Prog.
Notes: In terms of computational consideration, over 70% cares about the speed, suggesting the need to enhance the current capability of DEM. In addition to speed, they are also concerned with the physics that DEM can hand, including antiparticle force, particle shape and attrition. From 1 week to 1 month is time range that they are willing to wait for a DEM simulation to complete, giving us a guideline on the extent to enhance the current DEM codes.

## Slide 7: Outline
Objective: MFIX-DEM toward industrially relevant problems
Industrial Survey
Define Benchmark Cases
Profiling Benchmark Cases
Preliminary Results
Notes: To understand the current capability of MFIX-DEM, we have developed the following benchmarks

## Slide 8: Profiling MFIX-DEM: Benchmark cases
Settling
  Dense, enduring contacts
v (cm/s)
Square tumbler
Fluidized bed
Notes: Benchmark – settling system looks like particles not throughout 3D system – mention verbally why
-indicate at least verbally that cases contain range of dilute and dense, include instabilities (bubbling and clusters), etc.

## Slide 9: Profiling MFIX-DEM: Benchmark cases
v (cm/s)
Homogeneous cooling
v (cm/s)
  Dilute, nearly instantaneous collision
 = 45°
g
Riser flow
Ramp flow

## Slide 10: Outline
Objective: MFIX-DEM toward industrially relevant problems
Industrial Survey
Define Benchmark Cases
Profiling Benchmark Cases
Preliminary Results

## Slide 11: Profiling MFIX-DEM: Dense systems
Settling
Weak scaling analysis
Weak Scaling: change in CPU time with increasing np for an increasing problem size that scales with np
Contact force computation
Gas-solid coupling
Fluidized bed
Intel(R) Xeon(R) CPU X5660 @ 2.80GHz,
24 Processors per node, 24 GB RAM per node
MFIX-2015-1

## Slide 12: Profiling MFIX-DEM: Dilute systems
HCS
Weak scaling analysis
Riser flow
Intel(R) Xeon(R) CPU X5660 @ 2.80GHz,
24 Processors per node, 24 GB RAM per node
MFIX-2015-1
Gas-solid coupling
Fluid solver functions
Notes: stabilized biconjugate gradient (BiCGSTAB) method

## Slide 13: Profiling MFIX-DEM: Performance assessment
Loop metrics: Percentage of CPU time the benchmark simulations spend in vectorized loops, scalar loops, and outside of loops
Targeted improvements
Enhance vectorization  better utilization of single instruction, multiple data (SIMD) registers supported by current and future processors

## Slide 14: Profiling MFIX-DEM: Performance assessment
Miss ratio: the ratio of memory accesses that cause a cache miss.
Targeted improvements
  Reduce Level 2/Level 3 cache miss ratio  locality of data to the processors
Notes: L3 cache is just a larger, slower version of the L2 cache

## Slide 15: Outline
Objective: MFIX-DEM toward industrially relevant problems
Industrial Survey
Define Benchmark Cases
Profiling Benchmark Cases
Preliminary Results

## Slide 16: Preliminary Results: General floating point optimization (Drag calculation)
F = 10d0*phis/EPg**2 + EPg**2*(ONE+1.5d0*DSQRT(phis))
F = F + 0.413d0*RE/(24.d0*EPg**2) * (ONE/EPg + 3d0*EPg*phis + 8.4d0/RE**0.343) / (ONE+10.d0**(3d0*phis)/RE**(0.5+2.d0*phis))
Expressions with divisions and repeated operations in BVK drag
Optimize using
    Pre-calculated variables
    Avoid divisions
    Use a local cache for memory aligned access
local_array(1)=ONE/EPG/EPG
local_array(2)=ONE/EPG
local_array(3)=EPG
local_array(4)=EPG**2
local_array(5)=ONE/RE
F = 10d0*phis*local_array(1) + local_array(4)*(ONE+1.5d0*DSQRT(phis))

## Slide 17: Preliminary Results: Spatial sorting of particles
1
2
3
4
5
6
7
10
12
8
9
11
13
14
15
16
17
10
15
17
11
12
1
2
4
5
7
16
14
3
6
8
9
13
Spatial sorting (done at beginning of des time march)
 increase spatial data locality in memory while
    Finding neighbors
    Calculating inter particle forces
    Drag calculations
    Interpolating mean fields.

## Slide 18: Preliminary Results: State-based sorting of particles
Do i=1,MAX_PIP
If not a normal particle cycle
If nonexistent particle cycle
!Do operations
A(i) = B(i) + C(i)
End Do
n | n | ghst | X | n | n | ghst | X | n | n
Particle array
n | n | n | n | n | n | ghst | ghst | X | X
Sorted Particle array
Np_normal
General particle loop structure
With sorted particle Array
Remove “if” constructs to aid in vectorization
Use NP_NORMAL or MAX_PIP_EXIST
A = B + C
MAX_PIP_EXIST
Scalar loop
Vectorized loop

## Slide 19: Preliminary Results: Sorting and drag
Optimized code showed an overall ~10% improvement
Data cache misses reduced by 50%.
Parameters | Original | Optimized
L2 to L1 cache miss ratio (Data) | 0.369 | 0.149
L2 to L1 cache miss ratio (instruction) | 0.629 | 0.567
Square tumbler (~9000 particles on 20 x 20 x 5 grid)
Drag optimization
State based and spatial sorting
Spatial sorting
Notes: These are run on Intel Haswell cores on CU machine with intel 16 compiler. Compiler flags are –O2 –g. The cost of
Sorting is less than 1% of total run time. These results are from second quarterly report. The baseline run time is 530 sec for
~ 80000 des time steps.

## Slide 20: Preliminary Results: Fluid cell operations
Sorting
n | n | ghst | Np=0 | Np=0 | n | ghst | n | Np=0 | n
Cell data
ijkindex
n | n | n | n | n | ghst | ghst | Np=0 | Np=0 | Np=0
Cell data
Swap loop indices
Contiguous memory access
Removal of “if”
      Fluid_mask(ijk)=1 (if fluid_at)
      Fluid_mask(Ijk)=0 (otherwise)
Masking
1
2
3
4
5
6
7
8
9
i direction
j direction
      Extremely expensive

## Slide 21: Preliminary Results: Fluid cell operations
Serial HCS test case (~1200 particles)
Serial HCS test case (~33000 particles)
Compiler vectorizes subroutines like comp_mean_fields when the “if” conditions are removed. Time spent on fluid cell checks also reduce significantly.
Optimized code showed an overall ~30% improvement
Notes: These runs are on NREL machine using intel haswell cores and intel 16 compiler. Baseline hcs small case run took 610 seconds,
Baseline hcs big case took 3215 seconds.

## Slide 22: Summary
So far…
Profiling and optimization only applied to serial MFIX-DEM
Next steps…
Focus on improving parallel performance - i.e. tackling poor weak scaling in MFIX-DEM via
    Reducing MPI communication overhead
    Load-balancing
Industrially relevant problem demonstration
Uncertainty quantification

## Slide 23: Back up slide: Task list
Task 1 - Project Management and Planning
Task 2 - Profiling MFIX DEM
  Task 2a: Benchmark serial MFIX DEM
  Task 2b: Benchmark parallelized MFIX DEM
Task 3 - Determine Optimization Frameworks
Task 4 - Perform optimization and vectorization of serial DEM
  Task 4a: Employ optimization techniques
  Task 4b: Verify enhanced DEM code for numerical correctness
Task 5 - Optimize and enhance hybrid (MPI + accelerator) DEM
  Task 5a: Implement hybrid parallelization method (MPI + OpenMP)
  Task 5b: Use extensive parallel profiling to optimize parallel code
  Task 5c: Compare enhancements on multiple Xeon/Xeon Phi architectures
Task 6 - Industrially Relevant Problem
Task 6a: Survey of PSRI member companies
Task 6b: Experiments of Interacting Nozzles
Task 7 - Uncertainty Quantification
  Task 7a: Test Problem
  Task 7b: Challenge Problem
  Task 7c: Industrially Relevant Problem

## Slide 24: Back up slide: Computational Project Goals
Improve the computational performance of MFIX-DEM
  Create a set of benchmarks to guide optimization work
  Profile benchmarks
  Improve serial performance of select subroutines by a factor of 2
    Vectorization
    Optimization of memory access
  Improve parallel performance of MFIX-DEM
    Hybrid OpenMP + MPI parallelization
Demonstrate performance enhancements through DEM simulation with O(108) particles
Explore algorithmic changes

## Slide 25: Back up slide: Profiling MFIX-DEM: Summary
Current Capability
103 Np/core: Good speed for quick turn-around
104 Np/core: Slow, but likely acceptable
105 Np/core: Too slow for R&D turn-around
For a goal to simulate 108 particles
103 Np/core  105 cores: Unrealistic industrial
capability
104 Np/core  104 cores: Sweet spot, but serial speed
up needed and scalability for
cores >103
105 Np/core  103 core: MFIX-DEM too slow
Space for optimization to enable industrial relevant simulations
  Poor weak scaling
  Low vectorization of inner loops
  High number of cache misses

## Slide 26: Back up slide: Algorithm for spatial reordering of particles
dg_pic array is used to get the new ordering
Sorting_map and inverse sorting map is created
  sorting_map(1) = 6 (map from new id to old id)
  inv_sorting_map(1) = 10 (map from old id to new id)
  A copy of inverse sorting map is sorted
    a preferred sorting algorithm is used(quick sort/bubble sort)
    Particle data are swapped according to swaps in the sorting.
    The sorting maps are used to set the neighbor arrays

## Slide 27: Back up slide: Sorting neighbor arrays
2 | 3 | 4 | 5 | -
3 | 5 | 5 |  | 
4 |  |  |  | 
1
2
3
4
5
particles
neighbors
MFiX data structure
2
3
4
3
5
4
5
4
6
8
9
9
Neighbor information (human readable)
Neighbors(:)
Neighbor_index(:)
When sorting arrays based on state
  Particles are exchanged (ie say part. 1 becomes part. 4)
  When sorting neighbor arrays
    Need to populate new ids
    Need to adjust neighbor_index
    Need to offset sets of indices

## Slide 28: Back up slide: Swap loop indices
1
2
3
4
5
6
7
8
9
i direction
j direction
General loop structure
DO IJK = IJKSTART3,IJKEND3
I = i_of(ijk)
j = j_of(ijk)
k = k_of(ijk)
do kk=k,k+1
do jj=j,j+1
do ii=I,i+1
ijk2=funijk(ii,jj,kk)
do stuff
enddo
enddo
enddo
Exchange here!

## Slide 29: Profiling MFIX-DEM: Performance assessment
Loop metrics: Percentage of CPU time the benchmark simulations spend in vectorized loops, scalar loops, and outside of loops
Targeted improvements
Enhance vectorization  better utilization of single instruction, multiple data (SIMD) registers supported by current and future processors
Do i=1,MAX_PIP
If …
If …
A(i) = B(i) + C(i)
End Do
Do i=1,MAX_PIP
A(i) = B(i) + C(i)
End Do
OR
A = B + C
Scaler:
Vectorized: