## Slide 1
NETL Multiphase Flow Science Overview 2016
From Fundamentals to Cutting Edge
Bill Rogers
Multiphase Flow Science Team
August 09, 2016

## Slide 2: Team and Collaborators
MFS Team
S. Benyahia
G. Breault
K. Buchheit
J. Carney
J. Dietiker
J. Finn
R. Garg
A. Gel
B. Gopalan
C. Guenther
D. Huckaby
T. Jordan
H. Kim
A. Konan
Li
L. Lu
M. Meredith
Morris
J. Musser
P. Nicoletti
R. Panday
S. Rabha
W. Rogers
P. Saha
M. Shahnam
R. Singh
M. Syamlal
J. Tucker
D. Van Essendelft
A. Vaidheeswaran
V. Verma
J. Weber
Y. Xu
K. Yoo
Collaborators (PI)
G. Ahmadi (Clarkson)
I. Celik (WVU)
H. Emady (ASU)
C. Hrenya (UCB)
J. Hu (SNL)
V. Kumar (UTEP)
S. Mohaghegh (WVU)
J. De Wilde (UCL)
C. Roy (VT)
W. Spotz (SNL)
D. Tafti (VT)
C. Tong (LLNL)

## Slide 3: From Fundamentals to Cutting Edge
Fundamentals
  Grow the Multiphase Flow Science (MFS) program
  Continued focus on MFiX Software Suite Development
  Quality Assurance - VV&UQ efforts
  Multiphase Flow Analysis Laboratory to support validation
  Outreach to MFS stakeholders
Cutting Edge
  Simulation-based optimization using multiphase software

## Slide 4: Grow the MFS Program
MFS Funding has more than doubled in FY16 – now over $ 6 million!
  Advanced Gasification
  Coal and Coal-Biomass to Liquid
  Advanced Combustion
  Carbon Capture Simulation Initiative
  Innovative Process Technology
  Rare Earth Elements
MFS team members joining in FY16
  Christos Altantzis – Mechanical Engineering
  Subhodeep Banerjee – Mechanical Engineering
  Kyle Buchheit – Chemical Engineering
  Mary Ann Clarke –Mathematics
  Eli Heady – Computer Science
  Avinash Vaidheeswaran – Nuclear Engineering
  George Waldman –Mathematics
  Yupeng Xu – Chemical Engineering
  Liqiang Lu – Chemical Engineering
  Kisoo Yoo – Mechanical Engineering
  Justin Finn – Mechanical Engineer

## Slide 5: Two MFIX Releases
MFiX 2015-2 (Date: 10/27/2015)
  Autotools Build System - MFIX now uses autotools to configure and compile the code. This increases code portability while reducing overall script maintenance
  Semi-Explicit Coupling for DEM Simulation - A semi-explicit algorithm for coupled gas-solids flows was implemented in MFIX-DEM. This approach calculates gas-solids interaction forces during the gas phase time step resulting in decreased time to solution.
  Two New Continuum Momentum Equation Formulations
MFiX 2016-1 (Date: 04/13/2016)
  DMP support for DEM thermochemistry - MFIX-DEM simulations with heat transfer and/or chemical reactions now support parallel execution
    This allows for larger particle counts in reacting flow simulations with reduced time-to-solution for greater modeling capability of MFIX-DEM.
  DEM particle-wall heat transfer - MFIX-DEM particles may exchange heat with the domain boundaries via specified constant wall temperature boundary conditions
  Greater UDF capabilities - Users may construct user-defined functions (UDFs) to specify source terms to the governing equations and many transport coefficients and field properties
Prototype Circulating Fluid Bed Gasifier – full loop

## Slide 6: MFiX GUI
Demonstrated August 2013
Experimenting with 3D graphics (VTK), Sep 2013
Version 0.1 Released June 5, 2015
Today

## Slide 7: Geometry

## Slide 8: Background Mesh

## Slide 9: Regions

## Slide 10: Model Parameters

## Slide 11
MFIX Software Quality Assurance (SQA)
MFIX SQA goal is to perform systematic verification of MFIX features for correctness and numerical accuracy.
Documented in MFIX Verification and Validation Manual (https://mfix.netl.doe.gov/download/mfix/mfix_current_documentation/MDV3-VVUQ-v0.5.pdf)
Test cases (1) exercise one or more sub-models, (2) are computationally inexpensive, and (3) strive for maximum code coverage with minimal test overlap.
Source code managed in NETL hosted GitLab repository.
GitLab repository is monitored by Jenkins, a continuous integration (CI) server:
  Executes verification test suite after every commit
  Reports results via email and archives daily ‘snapshots’ of test case performance
Uncertainty Quantification efforts
  Fluid bed gasifier wraps up
  UQ efforts will concentrate on hydrodynamics,

## Slide 12: Multiphase Flow Analysis Laboratory
New Lab supporting model development and validation
Small-scale CFB
Granular hopper flow
Small bubbling beds with image analysis
Reacting beds:
fixed and bubbling
(CO2 Sorbents)
Particle separation and flow control
Particle characterization
Particle size distribution
Umf
Sphericity
Particle density, including skeletal and bulk
Porosity
Micrograph

## Slide 13
MFiX Stats FY16 (up to Aug. 2016)
  FY16 MFIX registrations = 362
    University = 257
    Industry = 48
    National Labs = 27
    Other = 30
  All-time MFIX registrations = 4,043
    University = 2,884
    Industry = 630
    National Labs = 209
    Other = 320
MFIX: 1,423 downloads
C3M: 126 downloads
MFIX GUI: 351 downloads

## Slide 14: Cutting Edge - Simulation-based Reactor Design and Optimization
Novel reactor designs will require understanding and control of reacting multiphase flows
The ability to accurately simulate reacting multiphase flow is needed for optimal design and operation
We are developing an Optimization Toolset based on multiphase Computational Fluid Dynamics (CFD)
  Uses the NETL MFiX Suite of multiphase CFD software for predicting reactor performance
  Demonstrate and validate optimal designs
Dense Flow
Dilute Flow
Dilute and Dense Flow
Regions
Solids Circulation

## Slide 15: Optimization Toolset (OT)
A prototype of the Optimization Toolset has been developed in FY16
  GUI-Based Software that manages the optimization process
Let’s look at a simple example application of OT for particle separation
  Any candidate REMS design will depend on manipulation of reacting particles for optimal performance, e.g.
    Coal “refining” – devolitilization requiring separation of coal/char/ash/volatiles;
    Gasification – control of coal/biomass/char/ash;
    Chemical looping combustion and gasification – control and separation of coal/biomass/char/ash/oxgen carrier
    Solid sorbent-based carbon capture – sorbent regeneration and thermal management

## Slide 16: Optimization Toolset (OT)
Use the OT and MFiX to optimize a batch separation – What is the optimal gas velocity to separate the particle mixture?
Gas Velocity Too Low - Under Fluidized
Gas Velocity Too High - Over Fluidized
Optimal Gas Velocity
Particles Randomly placed in initial state
2:1 Particle Density Ratio
4:3 Diameter Ratio
Rectangular Bed
Uniform gas velocity

## Slide 17: Application and Validation of the OT
3-D Printed Bed
Used to validate optimized batch separation example
Bed and Distributor Plate Assembly
Plenum
Plenum
Bed and Distributor Plate Assembly
Now - combine OT optimized design with additive manufacturing to 3D print the device and validate the results

## Slide 18: Application and Validation of the OT
Compare OT results to lab measurements – excellent qualitative agreement
  An image analysis-based technique being developed for quantitative comparison
Gas Velocity Too Low - Under Fluidized
Gas Velocity Too High - Over Fluidized
Optimal Gas Velocity

## Slide 19: Application and Validation of the OT
Let’s kick it up a notch – Use the OT to optimize a continuous separation device

## Slide 20: Application and Validation of the OT
e.g. Parametric Study of flow control

## Slide 21: Application and Validation of the OT

## Slide 22: Optimization Toolset – next steps
Application to reacting flows
  Reactor network models to handle complex chemistry
Implementation with full MFiX Suite of Software
Incorporate into new MFiX GUI
Continued validation with cold and reacting flows
Open source, public release

## Slide 23: MFS Team Presentations
Three Dimensional VOF Simulations for Wetting of Corrugated Sheet
Rajesh K. Singh and Janine E. Galvin
Particles Climbing Along a Vibrating Tube: Numerical Simulation using the Discrete Element Method (DEM)
Yupeng Xu, Jordan Musser, Tingwen Li, William A. Rogers
Coarse Grained Particle Method for Simulation of Liquid-Solids Reacting Flow
Liqiang Lu, Kisoo Yoo, Sofiane Benyahia

## Slide 24: Questions
Thanks for your time

## Slide 25: It’s All About a Clean, Affordable Energy Future
For More Information, Contact NETL
the ENERGY lab
Delivering Yesterday and Preparing for Tomorrow
National Energy Technology Laboratory
25