## Slide 1: Generic Framework for Modeling Radiative Heat Transfer in Gas-Solid Reacting Flows
Jian Cai
Assistant Professor
Department of Mechanical Engineering
University of Wyoming
jcai@uwyo.edu

## Slide 2: Combustion Research at UW
New combustion group
  3 junior faculty members
Expertise
  Laser diagnostic and spectroscopy
  Turbulent combustion (transported PDF)
  Multiphase radiation
  Heterogeneous reaction measurements

## Slide 3: Radiative Transfer Equation
Absorption
Emission
Outbound Scattering
Inbound Scattering

## Slide 4: Challenges
High dimensionality
  3 spatial dimensions: CFD discretization
  2 directional dimensions: RTE solvers
  1 spectral dimension: spectral models
Regimes: dimensionless optical thickness
  Extinction coefficient x length
  Optically thin: emission dominates
  Optically thick: mostly self absorbed
  Unity optical thickness: strongest interactions

## Slide 5: RTE solvers
Approximate directional variations
Spherical Harmonics (PN)
Discrete Ordinate Method (DOM)
  Easy to extend to high orders
  Expensive to model scattering
Photon Monte Carlo (PMC)
  Random sampling
  Expensive
  Validation

## Slide 6: Spectral properties
Gas: abrupt variations, multi-scales
Particle: depends on refractive index, size
CO2 10% 600K, Particle m=2.2-1.12i, fv=0.001
Cai, Modest, Powder Tech. 265, 76-82, 2014

## Slide 7: Spectral models
Gray
  Neglect spectral variations
Line-by-line
  Most accurate, accounts for all variations
  Most expensive, ~10 million spectral evaluations
Non-gray reduced models
  K-distribution methods
  Absorption Line Blackbody Distribution Function (ALBDF)
  Weighted Sum of Gray Gases (WSGG)

## Slide 8: Generic Framework for Gas Radiation
Flow fields previous step
Energy equation
Species equation
Momentum equation
Pressure equation
Radiation-combustion interface
Spectral model
RTE model
Gray
K-Distribution
Line-by-line
P1
Pn
DOM
PMC

## Slide 9: Comparing Models in Gas Flames
Investigate
  Nongray self-absorption
  Performance of k-distributions in inhomogeneous media
  Performance of P1, SPn RTE solvers
  Performance: accuracy, efficiency, robustness
Cai, Marquez, Modest, J. Heat Transfer. 136(11), 112702, 2014
T
CO2
H2O

## Slide 10: Generic Framework for Gas-Solid Flows
RTE
  Eulerian: Pn, DOM
  Lagrangian: PMC
Code name | Carrier phase | Dispersed phase | Dispersed radiative properties | Additional averaging? | RTE
E-E-E-E | Eulerian | Eulerian | Eulerian | No | Eulerian
E-E-E-L | Eulerian | Eulerian | Eulerian | No | Lagrangian
E-L-E-E | Eulerian | Lagrangian | Eulerian | Yes | Eulerian
E-L-E-L | Eulerian | Lagrangian | Eulerian | Yes | Lagrangian
E-L-L-L | Eulerian | Lagrangian | Lagrangian | No | Lagrangian

## Slide 11: Coal Flame Experiment
Pulverized coal
Lifted jet flame
Ignition by flue gas 1420 K
Re = 2500
Resembles major furnace flame features
E-L flame simulation with E-L-E-E radiation modeling
Coal
Air
Flue Gas

## Slide 12: Temperature and radiative source
Cai, Zhao, Modest, Haworth, TFESC-12950, 2015

## Slide 13: Pulverized coal flame
A similar coal ignition flame
Ignited by a methane flame
Close to optically thin
  Significant radiative heat loss
E-E simulation
3 solid phases

## Slide 14: Good agreements with experiments
Cai, Handa, Modest, Combust. & Flame, 162(4), 1550-1565, 2015

## Slide 15: Radiation impacts
Gas
Solid 16.6 um
24.8 um
35.9 um
Cai, Handa, Modest, Combust. & Flame, 162(4), 1550-1565, 2015

## Slide 16: MFIX-RAD
Open source release
  https://sourceforge.net/projects/mfix-rad/
MFIX-2016-1
Based on the generic framework
Capability
  Gray spectral
  P1 RTE

## Slide 17: Conclusions
Radiation is important to flame simulations
Radiation model = Spectral + RTE models
Complicated model combinations for multiphase flows
Generic framework helps to organize models