## Slide 1: Three dimensional VOF simulations for wetting of corrugated sheet
August 9 -10, 2016
NETL 2016 Workshop on Multiphase Flow Science, Morgantown, WV
Rajesh Singh and Janine Galvin-Carney
National Energy Technology Laboratory

## Slide 2: Background and Motivation
1http://www.epa.gov, IEA Report 2008, 3Chu S., Science, 2009, 5http://envis.tropmet.res.in, 4https://www.globalccsinstitute.com,
  CO2 Emissions from power plants needs to be mitigated !!
CO2 Separation and Capture Technology
Pre-combustion,
Oxy-fuel Combustion,
Membrane Separation,
Post Combustion.
~40% Emissions2
CO2 (72% Globally2)
More Efficient and Economical
Gaining Widespread Interest.
CO2 Separation and Capture Technology
Pre-combustion,
Oxy-fuel Combustion,
Membrane Separation,
Post Combustion.
Notes: This figure shows how annual average temperatures in the contiguous 48 states have changed since 1901. Surface data come from land-based weather stations. Satellite measurements cover the lower troposphere, which is the lowest level of the Earth’s atmosphere. “UAH” and “RSS” represent two different methods of analyzing the original satellite measurements. This graph uses the 1901–2000 average as a baseline for depicting change. Choosing a different baseline period would not change the shape of the data over time.

## Slide 3: CFD Modeling of Solvent Absorption
Challenges:
  Cannot model entire column focusing in on all physical phenomenon
  Multi-scale approach required
  TFM lacks suitable closure models for interphase interactions
Column2:
F ~10m
H ~30m
film thickness2
~ O(0.1mm)
Source4
Flue Gas
Lean Solvent
Purified
Gas
Rich Solvent
Layer height2:
~20cm
Corrugation height2:
O(mm)
CO2 absorption depends on
hydrodynamics of global & local flow
to Stripper
Study the hydrodynamics of rivulet flow over corrugated sheet
Column2:
F ~10m
H ~30m
Notes: Interactive parallel FLUENT simulation on ‘Joule’ Supercomputer

## Slide 4: Problem Setup
Sheets: arranged vertical & perpendicular to each other
FLEXIPAC Packing
(Representation)
s
B
h
α

100 mm
100 mm
Simulation
setup
Rivulet flow over vertical
corrugated sheet
Design Parameters of the Sheet | 
Corrugation angle () | 45
Crimp Angle () | 45
Corrugation base (B) | 18 mm
Corrugation height (h) | 9 mm
Corrugation side (s) | 12.73 mm
Frontal size | 100100 mm2

## Slide 5: VOF Method and Meshing
Challenges:
Mesh: 2.0  3.9 M
Time step:
Initially with
– Continuity and momentum equation of average phase
Governing Equations
– Transport equation for volume fraction
Force at interface due to Interfacial tension
Very fine mesh required; higher corrugation angles require even finer mesh
Very fine time steps

## Slide 6: Validation with Experiments
Corrugation angle: 45
(Subramanian & Wozny, IJCE, 2012, 838965)
1Nicolaiewsky & Fair, IECR, 1998. 38: 284-291.
All dimensions are in mm
Simulation conducted
only in this region
Perforations not modeled
Embossed surface in experiment not simulated
Embossing reduces contact angle1 ~2 smaller contact angle used in simulation
Notes: Gunter Wozny, Technische Universität Berlin, Berlin
Embossed sheet

## Slide 7: Validation with Experiments
Good agreement with experiments
Physical Properties of Liquids
Solvent | ml (mPa-s) | rl (kg/m3) | sl (mN/m) |  ()
Water | 1 | 997 | 72.7 | 76.6
Water-Glycerol | 4.6 | 1113 | 70 | 69
Silicon Oil | 4.6 | 915 | 18.5 | 7
S&W
Exp
CFD
Water
(386 mlpm)
Present
S&W
Exp
Glycerol/Water (387 mlpm)
Present
S&W
CCSI
Exp
Exp
Silicon Oil (241 mlpm)
Present

## Slide 8: Factors Affecting Film/Rivulet Flows
  Solvent properties and flow rate
    Viscosity () and surface tension () Kapitza number
  Contact angle ()
  Corrugation Angle
Depends on various parameters
Solvent | ml (Pa-s) | rl (kg/m3) | sl (N/m) | Ka
Water | 0.00089 | 997.0 | 0.07280 | 3969
30% MEA1 | 0.00252 | 1013.0 | 0.05480 | 750
40% MEA1 | 0.00371 | 1015.3 | 0.05500 | 450
0.07m MPZ2 | 0.00556 | 1005.3 | 0.05442 | 258
48.8% MDEA3 | 0.00925 | 1016.6 | 0.04756 | 117
0.51m MPZ2 | 0.01336 | 946.41 | 0.03437 | 50
0.41m MPZ2 | 0.02348 | 962.2 | 0.03589 | 25
0.31m MPZ2 | 0.03642 | 981.31 | 0.03840 | 15
Only depends on fluid properties
Independent of flow rate
1Maham, et al., Thermochimica Acta, 2002. 386: 111-118; 2Rayer, et al., J. Chem. Thermodynamics, 2011. 43: 1897-1905; 3Muhammad, et al., J. Chem & Engg. Data, 2008. 53: 2226-2229
Solvent Properties
Kapitza number (Ka)

## Slide 9: Temporal Gas-Liquid Interface (31MPZ)
pseudo-steady state: flow channeling
3.83
2.55
1.89
0.81
0.62
0.21
0.43
1.23

## Slide 10: Effects of Solvent Properties
Increasing
Normalized film thickness increases BUT absolute value decreases
Interfacial and wetted areas decrease
= viscous length scale
Increasing

## Slide 11: Effects of Contact Angle ()
Contact angle:
        A liquid exhibits different  with different solids
            water and steel: =70
            water and Plexiglas: = 81
        Roughness of the surface
        Value of contact angle inherently depends on surface tension
        A liquid with small  typically shows lower 
Increasing
Zisman Plot
Surface Tension (dyne/cm)
Two solvents representative of each regime
51MPZ (Ka=50) &
40MEA (Ka=443) &

## Slide 12: Effects of Contact Angle (g): 51MPZ (Ka=50)
Contact Angle= 20
Contact Angle= 80
Decreasing Contact Angle (g)
Interfacial area increases
Contact Angle= 50

## Slide 13: Effects of Contact Angle (g): 51MPZ (Ka=50)
Wetted & Interfacial Area
Increasing
Increasing contact angle (g):
Wetted and interfacial areas decrease
Film thickness increases
Film Thickness
Increasing

## Slide 14: Effects of Corrugation Angle (a): 51MPZ (Ka=50)
= 30
= 35
= 40
= 45
= 50
= 55
= 47.5
For fixed contact angle:
Corrugation angle
s
B
h
α


## Slide 15: Effects of Corrugation Angle (a)
51MPZ has a smaller surface tension () and therefore may exhibit smaller contact angles ()
only 51MPZ simulated
  Wetted area shows non-monotonic variation
  Optimum corrugation angle: 45
50
450
3969

## Slide 16: Conclusion
VOF simulations used to explore rivulet flow over corrugated sheet
Good agreement between experiments and VOF simulations
Results presented in terms of the Kapitza number:
Scaling relations for interfacial and wetted areas
  Solvent properties, flow rate and contact angle
  Interfacial area of rivulet
    decreases with increased Ka
    decreases with increased 
  Corrugation angle
  Non-monotonic variation of wetted area
  Optimum corrugation angle: 45
contact angle

## Slide 17
Acknowledgments
Disclaimer: This work is made available by an agency of the United States Government. Neither the United States Government, the Department of Energy, the National Energy Technology Laboratory, nor any of their employees, makes any warranty, express or implied, including warranties of merchantability and fitness for a particular purpose, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise, does not necessarily constitute or imply its endorsement, recommendation, or favor by the United States Government, the Department of Energy, or the National Energy Technology Laboratory. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government, the Department of Energy, or the National Energy Technology Laboratory, and shall not be used for advertising or product endorsement purposes.
Carbon Capture Simulation Initiative (CCSI)
NETL Supercomputer ‘Joule’
CCSI Task 3&4 Team

## Slide 19: Effect of Solvent Flow Rate (Q)
Solvent: 40MEA
(Ka=443)
DH = hydraulic diameter of inlet
Wetted & Interfacial Area
Film Thickness
Interfacial area and film thickness increase with increased flow rate

## Slide 20: Effects of Contact Angle: 51MPZ (Ka=50)
Interfacial area decreases
Snapshots of interface:
= 20
= 30
= 40
= 50
= 70
= 90
Increasing Contact Angle

## Slide 21: Interfacial and Wetted Area: 40MEA (Ka=448)
Film Thickness
Increasing
Increased contact angle (g):
Wetted and interfacial areas decrease
Film thickness increased
Wetted & Interfacial Area
Increasing

## Slide 22: Effects of Corrugation Angle (a)
increased corrugation angle enhanced sheet area
Actual area
L
W
Area of sheet with corrugation angle

## Slide 23: Effects of Corrugation Angle (a)
Film Thickness
film thickness unchanged
Wetted Area
wetted area shows non-monotonic variation

## Slide 24: Effects of Corrugation Angle (a) : 51MPZ (Ka=50)
For fixed contact angle:
= 55
= 50
= 47.5
= 40
= 35
= 30
= 45
Non-monotonic variation of wetted area