## Slide 1: Development of a comprehensive computational fluid dynamic (CFD) and discrete element model of biomass fast pyrolysis in a bubbling fluidized bed reactor
Ross Houstona, Oluwafemi Oyedejia, and Nourredine Abdoulmouminea,b
aBiosystems Engineering and Soil Science Department, University of Tennessee, Knoxville, TN 37996
bCenter for Renewable Carbon, University of Tennessee, Knoxville, TN 37996
Presented at NETL’s 2017 Workshop on Multiphase Flow Science

## Slide 2: Biomass Pyrolysis
Definition: Thermal decomposition of biomass in the absence of oxygen at moderate temperatures (450-600°C).
Produces three types of products:
  Solid (char)
  Condensable, organic liquid (bio-oil)
  Non-condensable gases (CO, CO2, H2, CH4)
Complex process:
  Varying feedstock composition
  Kinetics not fully understood
Notes: Speak on why biomass pyrolysis is an attractive renewable energy process
biomass availability
produces a liquid fuel product

## Slide 3: Rapid screening through simulation
Saves time and money
Allows for visualization and understanding of the complex environment inside the reactor
Applies conservation laws of mass, momentum, and energy to account for the coupling of transport types
Figure 1: Schematic of interactions between phases. Adapted from Mellin et al. (2013)
Heat
Momentum
Heat
Momentum
Heat
Momentum
Mass
Biomass (Solid)
Sand (Solid)
Fluid (Gas)

## Slide 4: Project Objective
The purpose of this research is to model biomass fast pyrolysis by utilizing a CFD model paired with a discrete element method (DEM) framework and existing comprehensive reaction schemes for pine and switchgrass feedstocks.
Particle Collision
Heat Transfer Model
Energy Transport
Devolatilization
Mass Transport
Momentum Transport
Figure 2. Examples of models needed to simulate fast pyrolysis through CFD.

## Slide 5: OpenFOAM
Free, open-source C++ CFD software
Completely modifiable code
Existing models for coal combustion
Ease of incorporating complex reaction kinetics
Potential to make the developed code available to the public
UTK High Performance Computer

## Slide 6: Why DEM?
Pros:
  Tracks each individual solid particle
  Allows for particle size distribution
  Irregular particle shape
  More accurate representation of what happens to biomass
Cons:
  Computationally expensive
  Slower than Eulerian-Eulerian
We are concerned with the affect physical properties of biomass particles have on biomass fast pyrolysis.

## Slide 7: Materials and Methods Experimental Setup
Bench scale bubbling fluidized bed reactor
  Diameter: 38.1 mm (1.5 in.)
  Height: 749.3 mm (29.5 in.)
Reaction temperature
  773 K
Two feedstocks
  Pine
  Switchgrass
Biomass inlet (total)
  10 g/min
Sand (total)
  200 g
Fluidizing gas velocity
  0.5 m/s
*Units in mm
Biomass Inlet
N2 Inlet
Sand
Figure 3. Reactor dimensions used for the CFD geometry.

## Slide 8: Materials and Methods Model Implementation
Velocity of Particle
Velocity of gas
Fluid Force
Particle/Wall Force
: Moment Exchange
Particle Volume
Gas Volume Fraction
Solid Volume Fraction
Gas Viscosity
: Gas Density
: Particle Diameter
: Drag Coefficient
: Particle Reynold’s Number
Mass Source
: Stress Tensor
Momentum Source
Energy
: Pressure
Thermal Diffusivity
Reaction Enthalpy Source
Particle Enthalpy Source
Radiation Source
Species Mass Fraction
: Mass Diffusion Constant
Particle Species Source
Reaction Species Source
Solid Phase (Lagrangian)
Fluid Force: Gidaspow Contact Force: Hertz-Mindlin (Hertzin Spring Dashpot Model)
Continuous Phase (Eulerian)
Turbulence Model: K-ε model
Mass Conservation:
Energy Conservation:
Momentum Conservation:
Chemical Species Conservation:

## Slide 9: Materials and Methods Submodels
Heat Transfer: Ranz Marshall
Particle Shrinkage Model:
Heterogeneous Reactions:
Combustion Model:
Partially Stirred Reactor (PaSR)
Transport Model: Newtonian
Constant viscosity
Phase Change:
Liquid Evaporation
Radiation Model: P1
Heat Transfer Constant
: Particle Volume Fraction
: Thermal Conductivity
Nusselt Number
Particle Diameter
: Prandtl Number
Gas Heat Capacity
Gas Viscosity
Particle Reynold Number
: Particle Mass
Particle Density
Particle Carbon Mass
: Time
Particle Surface Area
Gas Partial Pressure
Diffusion Rate Constant
Kinetic Rate Constant
: Mass Diffusion Constant
Particle Temperature
Gas Temperature
: Absorption coefficient
: Scattering coefficient
G: Incident radiation
: Linear-anisotropic phase function coefficient
Notes: PaSR-derives reaction rates in a transient manner based on a turbulent time scale as well as a kinetic time scale
https://openfoamwiki.net/images/8/8a/Christ_OFW6_slides.pdf

## Slide 10: Materials and Methods Reaction Scheme
Source: Mellin, P., Kantarelis, E., & Yang, W. (2014). Computational fluid dynamics modeling of biomass fast pyrolysis in a fluidized bed reactor, using a comprehensive chemistry scheme. Fuel, 117, Part A, 704-715. doi:http://dx.doi.org/10.1016/j.fuel.2013.09.009
Blondeau, J., & Jeanmart, H. (2012). Biomass pyrolysis at high temperatures: Prediction of gaseous species yields from an anisotropic particle. Biomass and Bioenergy, 41, 107-121. doi:https://doi.org/10.1016/j.biombioe.2012.02.016
Figure 4. Comprehensive pyrolysis reaction tree. Adapted from Mellin (2013).
Reaction |  | A (s-1) | E (kJ/mol) | ∆h (kJ/kg)
1 | Cellulose → Activated Cellulose | 8x1013 | 192.5 | 447.7
2 | Cellulose→ 5H2O + 6Char | 8x107 | 125.5 | -1087.8
3 | Activated Cellulose → Levoglucosan | 4T | 41.8 | 732.2
Table 1. Examples of the Primary pyrolysis reactions used in the CFD model
Reaction Rate: Modified Arrhenius
Note: Typical values for = 0

## Slide 11: Feedstock Characteristics
Two Feedstocks:
  Switchgrass
  Pine
Particle Diameter:
  Biomass: 0.85 mm
  Sand: 0.5 mm
Particle Density:
  Biomass: 600 kg/m3
  Sand: 2650 kg/m3
Component | (wt. %) | 
 | Switchgrass | Pine
Cellulose | 45.0 | 45.0
Hemicellulose | 27.0 | 26.0
Lignin-C | 6.7 | 8.8
Lignin-H | 6.7 | 8.8
Lignin-O | 6.7 | 8.7
Moisture | 3.7 | 2.0
Ash | 4.2 | 0.7
aHumbird, D., Trendewicz, A., Braun, R., & Dutta, A. (2017). One-Dimensional Biomass Fast Pyrolysis Model with Reaction Kinetics Integrated in an Aspen Plus Biorefinery Process Model. ACS Sustainable Chemistry & Engineering, 5(3), 2463-2470. doi:10.1021/acssuschemeng.6b02809
Table 1. Chemical composition of each feedstock by weight percenta.

## Slide 12
Results
Physical Properties-Switchgrass
Results
Physical Properties-Pine
Figure 5: Visualization of physical properties during pyrolysis of switchgrass for 6.00-6.92 seconds.
Figure 6: Visualization of physical properties during pyrolysis of pine for 6.00-6.52 seconds.

## Slide 13: Results Solids Evolution-Switchgrass
Figure 7: Production of intermediate solids during pyrolysis of switchgrass for 6.00-6.92 seconds.
Figure 8: Production of intermediate solids during pyrolysis of pine for 6.00-6.52 seconds.
Results
Solids Evolution-Pine

## Slide 14: Results Gas Evolution-Switchgrass
Figure 10: Vapor phase mass fraction, on a nitrogen free basis, of pine for 6.00-6.52 seconds.
Figure 9: Vapor phase mass fraction, on a nitrogen free basis, of switchgrass for 6.00-6.92 seconds.
Results
Gas Evolution-Pine
Yield:
50% of biomass has been converted to the gas phase
*Changes have been made to secondary reaction kinetics to slow down cracking

## Slide 15: Conclusions
Approximately 3 seconds is required for biomass particles to enter pyrolysis temperatures (723 K) and particles are approaching reaction temperatures (773 K)
Species evolution along the length of the reactor is as expected
  Increased NCG formation along the reactor as pyrolysis vapors undergo secondary cracking
The simulation has not reached steady state and most of the gases currently leaving the reactor are the light non-condensable gases
After the adjustment to the secondary reaction kinetics, bio-oil vapors are increasing in vapor mass fraction along the length of the reactor

## Slide 16: Plans for Future Work
Update kinetic reaction scheme for newest fast pyrolysis mechanisma
Optimize physical parameters such as maximum packing limit, coefficient of restitution, and fluidization velocity
Change biomass composition to reflect previous analyses by the Center for Renewable Carbon (CRC)
Validate results on bench scale reactor located in the CRC
aSource: Ranzi, E., Corbetta, M., Manenti, F., & Pierucci, S. (2014). Kinetic modeling of the thermal degradation and combustion of biomass. Chemical Engineering Science, 110, 2-12. doi:http://dx.doi.org/10.1016/j.ces.2013.08.014

## Slide 17: Acknowledgements
The U.S. Department of Agriculture (USDA), the National Institute of Food and Agriculture (NIFA), and the Agriculture and Food Research Initiative (AFRI)
  Grant number 2015-67021-24121.

## Slide 18: Thank you
Questions?