## Slide 1: Dakota Integrated with MFiX for UQ Analysis: Sensitivity of particle size on pressure drop in a fluidized bed DEM simulations
VMK Kotteda1*^, V Kumar2*, W Spotz3^,A Stephens3^,B Adams3^
1Postdoctoral Researcher, 2Associate Professor, 3Senior Research Staff
*University of Texas at El Paso, Sandia National Laboratories
2018 Multiphase Flow Science Workshop, August 7 – 9, 2018, Houston, USA

## Slide 2: Outline
Introduction
  Uncertainty quantification (UQ)
  Key statistics ideas
Dakota
  UQ methods
  UQ results (response function- bed height)
Implementation of MFiX in Dakota
  UQ results with Dakota-MFiX for fluidized bed ( 2 inputs,1 response fun)
  UQ results with Dakota-MFiX for fluidized bed ( 9 uncertain input variables, 2 response functions)

## Slide 3: Uncertainty Quantification
Why UQ?
Determine low order statistics
Find probability of reaching failure/success criteria
Assess range of possible outcomes
Ultimately, use simulations for risk-informed decision making,
e.g., assess how close uncertainty-endowed code predictions are to Experimental data
UQ is the process of
characterizing input uncertainties,
forward propagating these uncertainties through a computational model, and
performing statistical assessments on the resulting responses.
UQ process determines the effect of uncertainties on model outputs
Notes: uncertainty quantification (UQ) or nondeterministic analysis is the process of (1) characterizing input
uncertainties, (2) forward propagating these uncertainties through a computational model, and (3) performing
statistical or interval assessments on the resulting responses. This process determines the effect of uncertainties
and assumptions on model outputs or results. In Dakota, uncertainty quantification methods primarily focus on
the forward propagation and analysis parts of the process (2 and 3),

## Slide 4
Concept of a random variable x
Mean (
Standard deviation
Correlation coefficient Corr(x,y) =
realizations of random variables with
μ=100, σ=10
σ=50
Key Statistics Ideas
Positive correlation
Negative correlation
No correlation
x
y
y
y
x
x

## Slide 5
Dakota has grown significantly beyond an optimization toolkit.
  state-of-the-art optimization methods,
  methods for sensitivity analysis, parameter estimation, uncertainty quantification, and verification
The toolkit provides a flexible and extensible interface between simulation codes and iterative analysis methods.
Uncertainty in input variables u
Probability densities
Intervals
UQ method
Uncertainty in output f(u)
variability,
probabilities,
intervals (ranges)

## Slide 6: UQ methods
Consider variable characterizations, model properties, ultimate UQ goal to choose a method
Sampling (Monte Carlo, LHS)
Robust, understandable, and applicable to any model
Slow to converge
Moments, PDF/CDF, correlations, min/max
Reliability
Goal-oriented; target particular response or probability levels
Efficient local (require derivatives) / global variants
Moments, PDF/CDF, importance factors
Stochastic Expansions
Surrogate models tailored to UQ for continuous variables
Highly efficient for smooth model responses
Moments, PDF/CDF, Sobol indices
Epistemic
Non-probabilistic methods
Generally applicable, can be costly when no surrogate
Belief/plausibility, intervals, probability of frequency
Notes: Dakota can calculate the derivatives for you to use the reliability methods.

## Slide 7: A Practical Process for UQ
Identify uncertain input parameters
Characterize input uncertainties and map them into Dakota variable specifications
Select a method appropriate to variables, goal, and problem
Set up Dakota input file and interface to simulation
environment
method
sampling
sample_type lhs
samples = 1000
seed = 98765 rng rnum2
variables
normal_uncertain = 2
means = 0.80 0.80
std_deviaions = 0.10 0.10
descriptors 'x1' 'x2’
interface
fork
analysis_driver = 'mfix'
responses
response_functions = 1
no_gradients
no_hessians
Run study
Interpret the results

## Slide 8: MCS with 100,000 samples
Gel, A., Garg, R., Tong, C., Shahnam, M. and Guenther, C., 2013. Applying uncertainty quantification to multiphase flow computational fluid dynamics. Powder technology, 242, pp.27-39.
e p,n = particle-particle restitution co-efficient
e w,n = Particle-wall restitution co-efficient
Response function (Bed height) =
+ 0.18379 + 0.20556
Case # | Input1 e p,n | Input 2 e w,n | Bed height Sample mean | Bed height Sample Std deviation
1 | N(0.8,0.1) | N(0.8,0.1) | 14.371 | 1.7e-1
2 | N(0.8,0.1) | N(0.8,0.05) | 14.367 | 1.5e-1
UQ results with PSUADE
MCS with 100,000 samples
UQ results with Dakota
Flow in the fluidized bed
Surrogate model
Case # | Input1 e p,n | Input 2 e w,n | Bed height Sample mean | Bed height Sample Std deviation
1 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.7e-01
2 | N(0.8,0.1) | N(0.8,0.05) | 14.372 | 1.6e-1
Notes: We validated the results with Dakota.
The mismatch in case #2, could be due to rounding off the numbers in the formula.

## Slide 9: MCS with 100,000 samples
e p,n = particle-particle restitution co-efficient
e w,n = Particle-wall restitution co-efficient
Response function - bed height(h) =
+ 0.18379 + 0.20556
Case # | Input1 e p,n | Input 2 e w,n | Bed height Sample mean | Bed height Sample Std deviation
1 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.7e-01
2 | N(0.8,0.1) | N(0.8,0.05) | 14.372 | 1.6e-1
PCE (order =5) with different standard deviation specifications for input parameter distributions.
UQ results with Dakota
Case # | Input1 e p,n | Input 2 e w,n | Bed height Sample mean | Bed height Sample Std deviation
1 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.7e-01
2 | N(0.8,0.1) | N(0.8,0.05) | 14.372 | 1.6e-1
Notes: Compared the results with MC (sample size = 100000) and PCE (order =5) methods.

## Slide 10: MCS– sample size study
samples # | Input1 e p,n | Input 2 e w,n | h mean | h Std deviation
100,000 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.65e-01
10,000 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.65e-01
1000 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.65e-01
500 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.65e-01
200 | N(0.8,0.1) | N(0.8,0.1) | 14.374 | 1.66e-01
100 | N(0.8,0.1) | N(0.8,0.1) | 14.376 | 1.73e-01
50 | N(0.8,0.1) | N(0.8,0.1) | 14.372 | 1.59e-01
20 | N(0.8,0.1) | N(0.8,0.1) | 14.363 | 1.40e-01
10 | N(0.8,0.1) | N(0.8,0.1) | 14.356 | 1.32e-01
UQ results with Dakota
Notes: The effect of sample size on UQ statistics.

## Slide 11: Implementation of MFiX in Dakota
Identify uncertain input parameters
Characterize input uncertainties and map them into Dakota variable specifications
Select a method appropriate to variables, goal, and problem
Set up Dakota input file and interface to simulation
Run study
Create separate work directories for each independent run
Make the input file for MFiX simulations
Run MFiX simulations
Calculate the response functions
C++ Wrapper
Interpret the results

## Slide 12: Flow in the fluidized bed
Average bed height = 14.38 cm
Central jet fluidized bed using DEM simulations.
Central jet velocity = 4200 cm/s
Size of the Domain - 15cm x 90 cm
cells having width of 1 cm and height of 2 cm, resulting in a total of 675 (=15x45) computational cells.
The bed is initialized with 217.15 g of particles with a diameter of 0.4 cm and density of 2.7 g/cm3, resulting in total of 2400 spherical particles.
parameter | value
Particle-particle restitution co-efficient | 0.80
Particle-wall restitution co-efficient | 0.80
Notes: Show the instantaneous value.

## Slide 13: Dakota-MFiX results: Flow in a fluidized bed
Input 1 - e p,n | Input 2 - e w,n
N(0.8,0.07) | N(0.8,0.07)
Response function
Bed height =
PCE, Order =5
sample size =25
e p,n = particle-particle restitution co-efficient
e w,n = particle-wall restitution co-efficient
Mean
Std
14.41
3.62e-02
N p = Number of particles (=2400)
Y = y- coordinate of nth particle's position at time t
14.41
3.41e-02
LHS, sample size =500
Partial Correlation Matrix between input and output:
Bed height
ep,n 5.00894e-01
ew,n -2.28789e-01
Notes: Response function Std is 0.23% of mean
Input variables std is 5% of mean
Bed height for e p,n = 0.8 and e w,n = 0.8 is 14.38
Bed height from UQ is 14.41 – 0.03 = 14.38 14.32 – 0.06 = 14.26

## Slide 14: Dakota-MFiX results: Flow in a fluidized bed
e p,n = particle-particle restitution co-efficient
e w,n = particle-wall restitution co-efficient
Response function
1. Average bed height
Dp = Particle diameter
Uinlet = Velocity of the fluidizing agent at the inlet
KN = Particle – particle normal collision spring constant
KN_W = Particle – wall normal collision spring constant
MEW = Particle - particle friction co-efficient
MEW_W = particle – wall friction co-efficient
= Viscosity of the fluidizing agent at the inlet
2. Maximum pressure difference across the bed
Normal distribution, LHS, # of uncertain input variables = 9
 | Dp (cm) | Uinlet (cm/s) | e p,n | e w,n | KN (g/s2) | KN_W (g/s2) | MEW | MEW_W | (g/ cm s)
mean | 0.34 | 4200 | 0.8 | 0.8 | 1000000 | 1000000 | 0.1 | 0.1 | 0.00018
std | 0.0297 | 367.5 | 0.07 | 0.07 | 87500 | 87500 | 0.0087 | 0.0087 | 0.00001575
 | Dp (cm) | Uinlet (cm/s) | e p,n | e w,n | KN (g/s2) | KN_W (g/s2) | MEW | MEW_W | 
mean | 0.34 | 4200 | 0.8 | 0.8 | 1000000 | 1000000 | 0.1 | 0.1 | 0.00018
std | 0.0297 | 367.5 | 0.07 | 0.07 | 87500 | 87500 | 0.0087 | 0.0087 | 0.00001575

## Slide 15: Dakota-MFiX results: Flow in a fluidized bed
Response function
1. Average bed height
# of uncertain input variables = 9
2. Maximum pressure difference across the bed
Bed height at t=40 is 9.87 cm
Max pressure drop at t=40 is 15.99 k dn/cm2
 | Dp (cm) | Uinlet (cm/s) | e p,n | e w,n | KN (g/s2) | KN_W (g/s2) | MEW | MEW_W | (g/ cm s)
 | 0.34 | 4200 | 0.8 | 0.8 | 1000000 | 1000000 | 0.1 | 0.1 | 0.00018
 | Dp (cm) | Uinlet (cm/s) | e p,n | e w,n | KN (g/s2) | KN_W (g/s2) | MEW | MEW_W | 
 | 0.34 | 4200 | 0.8 | 0.8 | 1000000 | 1000000 | 0.1 | 0.1 | 0.00018

## Slide 16: Response function – bed height
Mean:
Std:
Normal distribution
9.6827
1.9529
, LHS, sample size = 500
Partial Correlation Matrix between
input and output:
Bed height
9.87853e-01
7.65915e-01
1.26841e-03
-2.19558e-02
-5.44667e-02
-4.08984e-02
-1.03671e-02
6.74702e-02
-1.76986e-02
Dp
Uinlet
e p,n
e w,n
KN
KN_W
MEW
MEW_W

## Slide 17: Response function – Max pressure drop across the bed
Normal distribution
, LHS, sample size = 500
Mean:
Std:
1.5857e+04
5.2590e+03
Partial Correlation Matrix between
input and output:
Pressure drop
9.81640e-01
-4.91593e-01
5.73839e-02
1.11189e-01
-7.00940e-02
-1.14437e-02
3.87739e-02
3.50937e-02
-2.23406e-02
Dp
Uinlet
e p,n
e w,n
KN
KN_W
MEW
MEW_W

## Slide 18: Dakota-ML results: Flow in a fluidized bed
Normal distribution, LHS, sample size = 100,000
Response function - Max pressure difference across the bed
DNN
Variance = 0.96
Mean:
Std:
Deep Neural Network
(training sample size=400,
N(0.8,0.07), …..
Testing sample size = 100
N(0.8,0.07), ….
1.5294216466e+04
2.7316445141e+03
1.53791e+04
2.99497e+03
global regression
orthogonal polynomial
Approximation
1.5854484429e+04
+ 5.1191312475e+03 Dp
-5.6223801405e+02 Uinlet
+ 1.0102024535e+02 e p,n
+ 1.1853996506e+02 e w,n
+ 5.2048560208e+02 Dp*Dp
+ 1.8268743945e+02 Dp* Uinlet
+ 1.8787829466e+02 Uinlet * Uinlet
Notes: Response function Std is 0.23% of mean 0.17% of mean
Input variables std is 5% of mean
Bed height for e p,n = 0.8 and e w,n = 0.8 is 14.38
Bed height from UQ is 14.41 – 0.03 = 14.38 14.41 – 0.03 = 14.38

## Slide 19: Acknowledgement
Thank you

## Slide 21
P1
P2
Pn
Tree 1
Tree 2
Tree n
Random Forest is a supervised learning algorithm.
It is a flexible, easy to use machine learning algorithm that produces, even without hyper-parameter tuning, a great result most of the time.
It is also one of the most used algorithms, because it’s simplicity and the fact that it can be used for both classification and regression tasks.
It is derived from decision trees. Instead of applying decision tree algorithm on all dataset, dataset is separated into subsets and same decision tree algorithm is applied to these subsets.
Decision is made by the highest number of subset results.
ensemble of decision Trees
creates a forest and makes it somehow random.
Random Forest Algorithm

## Slide 22
This can be represented as
To get the result from the sum, we apply the activation
function, sigmoid, to each element:
4x3
4x3
Sigmoid hidden layer sum = hidden layer result
4x3
w1
w2
w3
w4
w5
w6
w7
w8
w9
hidden layer result x w7 w8 w9
= [output]
Sigmoid
3x1
X
=
hidden layer sum
0,0,1,1
0,1,0,1
Input layer
Hidden layer
Output
Neuron
It is one of the widely used machine learning algorithms
Artificial Neural Networks (ANN) are biologically inspired networks for performing certain specific tasks such as regression.
ANN is similar to neural networks in two ways: acquire knowledge through training and apply the knowledge within inter-neuron connection strengths known as weights.
ANN and more complex deep learning techniques are some of the tools for solving very complex problems.
Deep Neural Network
Notes: The forward propagation process is a series of sum products and transformations. Let’s calculate the first hidden sum with all four input data:
We do this for every node in the hidden layer, and this becomes our input for the next layer, our output layer. After applying the activation function on the output node value, this is what we interpret as the output of the neural network. It will probably be off from what it should be because the initial weights are random and that will give us a random answer. But that leads us to the next process, which will help us find the right weights