## Slide 1: Exploiting multiphase slug flow for controlled manufacturing of uniform crystals
Mo Jiang

## Slide 2: Enhance quality control and process efficiency
Jiang et al., The role of automatic process control in Quality by Design. In Comprehensive Quality by Design for Pharmaceutical Product Development and Manufacture, John Wiley & Sons, Hoboken, NJ, 2017.
Quality (e.g., color, bioavailability)
Washing, filtration, and milling
Formulation (e.g., tableting)
Crystal size distribution (CSD) and shape/morphology
Challenges of CSD control
Simultaneous crystallization phenomena (e.g., growth, particle attrition, agglomeration, polymorphism, and secondary nucleation)
Batch-to-batch variability
Scale-up and operational problems
2

## Slide 3
Towards novel efficient and cost-effective crystallizers suitable for both development and manufacturing
Process intensification for continuous crystallization would
Minimize scale-up problems and time/cost, while retaining the advantages of the best previous continuous crystallizers
 This criterion would be met if the hydrodynamics provided sufficient mixing to replace mixing blades
 This criterion would be met if the hydrodynamics was consistent at both lab and production scales
Minimize operational problems (e.g., attrition, clogging)
3

## Slide 4
Approach: Exploit multiphase hydrodynamics
Plug
Stratified
Wavy
Slug
Dispersed bubble
Annular
worldofstock.com
Ghajar. J. Braz. Soc. Mech. Sci., 27 (1), 46–73, 2005.
4

## Slide 5: Slug flow for crystallization
Operate under conditions where slugs spontaneously form
Grow crystals within each slug
Uniform T and C in each slug
Reduce scale-up risk (use same slug and tube dimensions at lab and production scales)
Separate control of crystal nucleation and growth
Video, slowed by 8 times
5

## Slide 6: Slug-flow crystallization process design
Nucleation
Controlled Growth
Temp 4
Temp 3
Temp 2
Temp 1
Slurry
Air
Air
Slurry
Air
Slurry
Air
Slurry
Solution
A
Solution B
Slug formation
Control dissolution and growth
in slugs
Achieve target CSD (e.g., uniform crystals)
Nucleate crystals (e.g., in micromixers)
Generate liquid slugs
in tubing
Use spatially varying
temperature profile
Control nuclei
number density
6

## Slide 7: Demonstration of slug-flow crystallization
Temp 4
Temp 3
Temp 2
Temp 1
Slurry
Air
Air
Slurry
Air
Slurry
Air
Slurry
Hot solution
Cold solution
LAM slurry
Air
Slug
Video
Video
LAM: L-asparagine monohydrate
High tendency to aggregate in H2O
7
Handle high
solids density

## Slide 8
Laminar flow
Coaxial mixer
Temp 4
Temp 3
Temp 2
Temp 1
Slurry
Air
Air
Slurry
Air
Slurry
Air
Slurry
Hot solution
Cold solution
Improvement of mixing hydrodynamics to increase seed size uniformity
200 µm
200 µm
200 µm
8

## Slide 9
Radial mixers
Mixer criteria
Reproducible operations
Min-leakage connection
Minimize clogging
Coaxial mixer
Micromixer prototypes for seed generation
9

## Slide 10
Improvement of slug aspect ratio to promote mixing
Aspect ratio ~ 1
Tubing wall
Tubing wall
Video is 16 times slower than real time.
Video
Crystals in slugs with aspect ratio closer to 1 are more spread out in the slug, more like a batch crystallizer.
The solution is better mixed with higher flow rate.
Aspect ratio goes up to 4
Video
Tubing wall
Tubing wall
1 mm
1 mm
Flow direction
10

## Slide 11: Nucleation in coaxial mixer and growth in slugs
Representative slug
Coaxial mixers improved crystal uniformity, morphology, and reduced aggregation compared to laminar flow
11
Uncontrolled cooling

## Slide 12: Summary
Designed experimental system to spontaneously generate stable slugs with controlled aspect ratio, where the temperature and concentration are uniform due to recirculation
Generated high-quality large uniform crystals from a cooling slug-flow crystallizer, with low scale-up risk
Enhanced size uniformity by improving nucleation with coaxial or radial mixers, and improving growth by setting a controlled spatial temperature profile
12

## Slide 13: Acknowledgments
Richard D. Braatz

## Slide 14
Operate in stable regime for self-induced slug flow
Tubing I.D. = 4 mm
My slug flow operation (3.1 mm I.D.)
Gas velocity (m/s)
Liquid velocity (m/s)
Barnea, Luninski, and Taitel. Can. J. Chem. Eng., 61 (5), 617–620, 1983.
5

## Slide 15
Crystals with nucleation from cooling micromixers
15
Coaxial mixer
500 μm
Radial mixer

## Slide 16: Crystal growth improvement with heating stage
No heating stage
Heating in aluminum tubing
Cooling in two temperature baths
Heating in aluminum tubing
Cooling in air
Add heating stage
Controlled cooling stage
500 µm
500 µm
500 µm
16

## Slide 17: Slug size uniformity improvement by tube orientation
Temp 4
Temp 3
Temp 2
Temp 1
Slurry
Air
Air
Slurry
Air
Slurry
Air
Slurry
Hot solution
Cold solution
LAM slurry
Air
Slug
Video
17

## Slide 18
M. Jiang, et al. Continuous-flow tubular crystallization in slugs spontaneously induced by hydrodynamics. Crystal Growth & Design, 14 (2), 851–860, 2014.
Nucleation in radial mixer and growth in slugs
Slugs #106-108
Slugs #286-288
Radial mixers also reduced aggregation compared to laminar flow