## Slide 1: Offline Evaluation of Agglomeration Tendency with a Gas-Solid Fluidized Bed of Identical Wet Particles: Model Development and Integration with MFiX
J. Shabaniana, M. Duchesnea, A. Runstedtlera, M. Syamlalb, R. Hughesa
a Natural Resources Canada, CanmetENERGY-Ottawa, 1 Hannel Drive, Ottawa, Ontario K1A 1M1, Canada
b National Energy Technology Laboratory, U.S. Department of Energy, Morgantown, West Virginia 26507-0880, United States

## Slide 2: Background
Pressurized oxy-fuel combustion:
Figure adapted from Seddighi et al., Appl. Energy 232 (2018) 527-542.

## Slide 3: Background (Cont.)
Particle agglomeration:
http://www.balajiminerals.in/silica-sand.htm
Shabanian et al., Energy Fuels 33 (2019) 1603-1621.
Figure adopted from Bartels et al., Energy Fuels 23 (2009) 157-169.
@ 900oC

## Slide 4: Background (Cont.)
IPFs: Interparticle forces

## Slide 5: Building Block for Agglomeration Phenomenon
Binary, identical wet particle collision
(Has since been extended to non-identical particles)
(capillary/static force): liquid surface tension acting on the liquid-solid boundary + reduced hydrostatic pressure in the bulk of liquid bridge
(viscous/dynamic force): relative movement between colliding objects, pressure distribution in the liquid bridge along the direction, viscous dissipation
IPFs due to the liquid bridge:
Pitois et al., Eur. Phys. J. B 23 (2001) 79-86.
Shabanian et al., Chem. Eng. Sci. (2019) Submitted for publication.

## Slide 6: Reference Frame
Handle collision of particles having different collision speeds with respect to the frame :
Equation of motion:
Pitois et al., Eur. Phys. J. B 23 (2001) 79-86.
Shabanian et al., Chem. Eng. Sci. (2019) Submitted for publication.

## Slide 7: This Study’s Energy Balance Model
, , , , , constant , constant , ,
, , , , , , , , (), , ,
Rebound
, ,
Agglomeration
Agglomeration
…
Agglomeration
…
Yes
No
Yes
No
Yes
No
Rebound
or
Inputs:
, , , , , , , , , , , ,
, ,
This study’s viscous loss expressions:
Shabanian et al., Chem. Eng. Sci. (2019) Submitted for publication.
Notes: , , ,
𝑨=𝟑/𝟐 𝝅𝝁〖𝒓_𝒑〗^𝟐 𝒗_𝟎 , 𝒇(𝑫)=√(𝑫^𝟐+𝒂^𝟐 )/(𝑫+√(𝑫^𝟐+𝒂^𝟐 ))^𝟐 , 〖𝑺𝒕〗_𝒗=(𝟐𝒎_𝒑 𝒗_𝟎)/(𝟑𝝅𝝁〖𝒓_𝒑〗^𝟐 ) ,

## Slide 8: Darabi et al. vs. This Study
Darabi et al., Chem. Eng. Sci. 64 (2009) 1868-1876.
Darabi et al.’s agglomeration model
Models
This study’s agglomeration model
Darabi et al.’s model | This study
Reasonable outcomes under capillary limiting conditions and not under viscous limiting conditions. | Reasonable outcomes under both capillary and viscous limiting conditions with highly wetting systems.
Particle velocity during the collision changes due merely to the viscous loss and solid-solid contact loss. | Accounts for the contribution of capillary force in the approach stage when estimating the initial particle speed for the separation stage.
Employs the correlation proposed by Lian et al. (1993) to estimate the liquid bridge rupture distance under both static and non-static conditions. | Employs the correlation proposed by Pitois et al. (2001) to estimate the liquid bridge rupture distance under both static and non-static conditions.
Evaluates the collision outcome at the point of liquid bridge rupture. | Evaluates the collision outcome in three steps based on the values of kinetic energy parameters (computationally more efficient).
Darabi et al.’s viscous loss expression:
This study’s viscous loss expression:
Darabi et al.’s expression:
Pitois et al., Eur. Phys. J. B 23 (2001) 79-86.
Lian et al., J. Colloid Interface Sci. 161 (1993) 138-147.
Shabanian et al., Chem. Eng. Sci. (2019) Submitted for publication.
This study’s expression:
Notes: 𝑪𝒂=〖𝝁𝒗_𝒓𝒆𝒍〗∕𝜸

## Slide 9: Darabi et al. vs. This Study (cont.)
Input parameters to evaluate the performances of the original and improved agglomeration models for two reference cases |  | 
 | Case I: water | Case II: hypothetical slag
Diameter of a solid particle, (µm) | 800 | 800
Particle density, (kg/m3) | 2650 | 2650
Dry restitution coefficient, (-) | 0.90 | 0.90
Height of a surface asperity, (µm) | 0.10 | 0.10
Thickness of the coating layer, (µm) | 5.00 | 0.15
Liquid viscosity, (Pa.s) | 8.9 × 10-4 | 10.0
Surface tension, (N/m) | 0.073 | 0.400
Contact angle, (deg) | 10 | 10
Input parameters to evaluate the performances of the original and improved agglomeration models for two reference cases |  | 
 | Case I: water | Case II: hypothetical slag
 | 800 | 800
 | 2650 | 2650
 | 0.90 | 0.90
 | 0.10 | 0.10
 | 5.00 | 0.15
 | 8.9 × 10-4 | 10.0
 | 0.073 | 0.400
 | 10 | 10
Base particle: silica sand
Binary collision of identical wet particles:
Darabi et al., Chem. Eng. Sci. 64 (2009) 1868-1876.
Darabi et al.’s agglomeration model
Models
This study’s agglomeration model
Shabanian et al., Chem. Eng. Sci. (2019) Submitted for publication.

## Slide 10: Darabi et al. vs. This Study (cont.)
Darabi et al.’s model
Slag
Water
This study’s model
: critical particle speed
Experimental trends
Figure adapted from Gollwitzer et al., Phys. Rev. E 86 (2012) 011303.
Experimental data from a wet collision between a spherical glass bead and a roughened plate.
M5: Silicone oil
Density: 925 (kg/m3)
Viscosity: 4.6 (mPa.s)
Surface tension: 19.2 (mN/m)
Film thickness: 1 (mm)
Figure adapted from Gondret et al., Phys. Fluids 11 (1999) 2803-2805.
Experimental data from a wet collision between a steel bead and a roughened plate.

## Slide 11: Sensitivity Analysis
Asperity height
Particle size
Thickness of coating layer
: critical particle speed
Slag
Water
Reference
Reference
Reference for slag

## Slide 12: Sensitivity Analysis (cont.)
Liquid viscosity
Surface tension
Particle density
: critical particle speed
Reference
Silica sand
Olivine
Ilmenite
Slag
Water

## Slide 13: Particle Asperity Characteristics & Wet Particle Agglomeration
HA
HHA
Shabanian et al., Powder Technol. 316 (2017) 139-147.
LaMarche et al. theory:
LaMarche et al., Chem. Eng. Sci. 158 (2017) 140-153.
Dual superimposed submerged spherical asperities
Measurement with the help of Atomic Force Microscope (AFM) topological surface map
Integrate agglomeration model with particle asperity characteristics:
1
2
3
: thickness of coating layer
& : height and radius of small asperity, respectively
& : height and radius of large asperity, respectively
: radius of a solid particle
HA: High Alarm
HHA: High-High Alarm
Defluidized bed

## Slide 14: Offline Evaluation of Wet Collision Outcome
CFD-DEM of a fluid bed with no IPFs in MFiX

## Slide 15: MFiX CFD-DEM Simulation
Simulation parameters | Solid information | Gas information | Bed geometry
Material | Silica sand | Air | 
Diameter of a solid particle, (µm) | 800 |  | 
Particle density, (kg/m3) | 2650 |  | 
Dry restitution coefficient, (-) | 0.90 |  | 
Number of particles (-) | 28336 |  | 
DEM time step (s) | 1.1849e-6 (calculated) |  | 
Temperature, (oC) |  | 850 | 
Pressure, (Pa) |  | 101325 | 
Superficial gas velocity (m/s) |  | 1.50 | 
Gas density, (kg/m3) |  | 0.3146 | 
Gas viscosity, (Pa.s) |  | 46.835e-6 | 
CFD time step (s) |  | 1.0e-3 | 
Column ID (m) |  |  | 0.0254
Column height (m) |  |  | 0.1500
Fixed bed height (m) |  |  | 0.0296
Gas distributor type (-) |  |  | Porous plate
Simulation parameters | Solid information | Gas information | Bed geometry
Material | Silica sand | Air | 
 | 800 |  | 
 | 2650 |  | 
 | 0.90 |  | 
Number of particles (-) | 28336 |  | 
DEM time step (s) | 1.1849e-6 (calculated) |  | 
 |  | 850 | 
 |  | 101325 | 
Superficial gas velocity (m/s) |  | 1.50 | 
 |  | 0.3146 | 
 |  | 46.835e-6 | 
CFD time step (s) |  | 1.0e-3 | 
Column ID (m) |  |  | 0.0254
Column height (m) |  |  | 0.1500
Fixed bed height (m) |  |  | 0.0296
Gas distributor type (-) |  |  | Porous plate
Biggest challenge: Number of particles (computational cost)
e.g.,
Column ID (m) | Fixed bed height (m) | Fixed bed voidage (-) | Particle diameter (µm) | Number of particles
0.0508 | 0.120 | 0.45 | 550 | 1535784
0.0508 | ~ 0.120 | 0.45 | 300 | 9454440

## Slide 16: Post-Processing Procedure
Figure adopted from Garg et al., MFiX-DEM Documentation (2012).
Neighbor search algorithm:
Verlet list of target particle:
2D case: particles belonging to 9 surrounding cells
3D case: particles belonging to 27 surrounding cells
Colliding particles at impact condition:
Post-processing of collision outcomes using a cylindrical mesh:
= -
Distance between surfaces of target and neighbor particles = (e.g., µm)
Approaching particles:
Evaluate the collision outcome by integrating the agglomeration model with particle asperity characteristics
Collision frequency: =
Collision frequency weighted averaging of the information over 3D annulus and present the result in a 2D cell

## Slide 17: Case Studies
Simulation parameters | Solid information | Gas information | Liquid information |  | 
 |  |  | Case Study 1 | Case Study 2 | Case Study 3
Material | Silica sand | Air | V2O5 | V2O5 | V2O5
Diameter of a solid particle, (µm) | 800 |  |  |  | 
Particle density, (kg/m3) | 2650 |  |  |  | 
Height of small asperity, (µm) | 9.085e-3 |  |  |  | 
Radius of small asperity, (µm) | 1.935 |  |  |  | 
Height of large asperity, (µm) | 1.090e-1 |  |  |  | 
Radius of large asperity, (µm) | 10.319 |  |  |  | 
Temperature, (oC) |  | 850 |  |  | 
Pressure, (Pa) |  | 101325 |  |  | 
Superficial gas velocity (m/s) |  | 1.50 |  |  | 
Liquid density, (kg/m3) |  |  | 2250 | 2250 | 2250
Liquid viscosity, (Pa.s) |  |  | 0.01 | 0.01 | 0.001
Surface tension, (N/m) |  |  | 0.10 | 0.10 | 0.10
Contact angle, (deg) |  |  | 10 | 10 | 10
Thickness of the coating layer, (µm) |  |  | 0.050 | 0.150 | 0.150
Simulation parameters | Solid information | Gas information | Liquid information |  | 
 |  |  | Case Study 1 | Case Study 2 | Case Study 3
Material | Silica sand | Air | V2O5 | V2O5 | V2O5
 | 800 |  |  |  | 
 | 2650 |  |  |  | 
 | 9.085e-3 |  |  |  | 
 | 1.935 |  |  |  | 
 | 1.090e-1 |  |  |  | 
 | 10.319 |  |  |  | 
 |  | 850 |  |  | 
 |  | 101325 |  |  | 
Superficial gas velocity (m/s) |  | 1.50 |  |  | 
 |  |  | 2250 | 2250 | 2250
 |  |  | 0.01 | 0.01 | 0.001
 |  |  | 0.10 | 0.10 | 0.10
 |  |  | 10 | 10 | 10
 |  |  | 0.050 | 0.150 | 0.150
Case study 4:
Liquid properties the same as case study 2.
Assume and are 0.050 and 0.500 µm, respectively (for a more irregular particle).
*
* Particle asperity characteristics were assumed to be 2.5 times larger than those reported for spherical soda-lime glass particles of 69 µm in size in:
Liu et al., Chem. Eng. Sci. 145 (2016) 266-278.

## Slide 18: Results – Case Study 1 – Thin Coating Layer
0.0007 m/s
Notes: 0.00068 m/s
𝒗_𝟎^∗= 0.00068 m/s
In the “occupancy profile of collision frequency weighted volume corrected fractional collision occurrence”, for the dark red cell we have: 𝒗_𝟎= 0.0000479 m/s and in the dark brown cell we have: 𝒗_𝟎= 0.005 m/s. For these two cells (or four cells that obtained after mirroring) we have a very high collision frequency values while the values of 𝒗_𝟎 are reasonable and within the range of 𝒗_𝟎 values detected in other neighboring cells. As we calculated the collision frequency based on (1/t_col) and t_col was calculated based on the “distance between surfaces of colliding particles/(2𝒗_𝟎)”, there is a chance that we had a few collisions where the particles were extremely close together, which resulted into a very small value of t_col. Hence, we could have a very large value of (1/t_col). Based on the 𝒗_𝟎 values reported above for the mentioned cells and that of 𝒗_𝟎^∗ under the conditions of study here, it is rational to only have one cell with a dark brown color in the “occupancy plot of collision frequency weighted volume of corrected agglomerating collision occurrence”.

## Slide 19: Results – Case Study 2 – Thicker Coating Layer
0.005 m/s
Notes: 0.00486 m/s
𝒗_𝟎^∗= 0.00068 m/s
In the “occupancy profile of collision frequency weighted volume corrected fractional collision occurrence”, for the dark red cell we have: 𝒗_𝟎= 0.0000479 m/s and in the dark brown cell we have: 𝒗_𝟎= 0.005 m/s. For these two cells (or four cells that obtained after mirroring) we have a very high collision frequency values while the values of 𝒗_𝟎 are reasonable and within the range of 𝒗_𝟎 values detected in other neighboring cells. As we calculated the collision frequency based on (1/t_col) and t_col was calculated based on the “distance between surfaces of colliding particles/(2𝒗_𝟎)”, there is a chance that we had a few collisions where the particles were extremely close together, which resulted into a very small value of t_col. Hence, we could have a very large value of (1/t_col). Based on the 𝒗_𝟎 values reported above for the mentioned cells and that of 𝒗_𝟎^∗ under the conditions of study here, it is rational to only have one cell with a dark brown color in the “occupancy plot of collision frequency weighted volume of corrected agglomerating collision occurrence”.

## Slide 20: Results – Case Study 3 – Lower Viscosity Liquid
0.005 m/s
Notes: 0.00462 m/s
𝒗_𝟎^∗= 0.00068 m/s
In the “occupancy profile of collision frequency weighted volume corrected fractional collision occurrence”, for the dark red cell we have: 𝒗_𝟎= 0.0000479 m/s and in the dark brown cell we have: 𝒗_𝟎= 0.005 m/s. For these two cells (or four cells that obtained after mirroring) we have a very high collision frequency values while the values of 𝒗_𝟎 are reasonable and within the range of 𝒗_𝟎 values detected in other neighboring cells. As we calculated the collision frequency based on (1/t_col) and t_col was calculated based on the “distance between surfaces of colliding particles/(2𝒗_𝟎)”, there is a chance that we had a few collisions where the particles were extremely close together, which resulted into a very small value of t_col. Hence, we could have a very large value of (1/t_col). Based on the 𝒗_𝟎 values reported above for the mentioned cells and that of 𝒗_𝟎^∗ under the conditions of study here, it is rational to only have one cell with a dark brown color in the “occupancy plot of collision frequency weighted volume of corrected agglomerating collision occurrence”.

## Slide 21: Results – Case Study 4 – Larger Asperity
0.001 m/s
Notes: 0.00104 m/s
𝒗_𝟎^∗= 0.00068 m/s
In the “occupancy profile of collision frequency weighted volume corrected fractional collision occurrence”, for the dark red cell we have: 𝒗_𝟎= 0.0000479 m/s and in the dark brown cell we have: 𝒗_𝟎= 0.005 m/s. For these two cells (or four cells that obtained after mirroring) we have a very high collision frequency values while the values of 𝒗_𝟎 are reasonable and within the range of 𝒗_𝟎 values detected in other neighboring cells. As we calculated the collision frequency based on (1/t_col) and t_col was calculated based on the “distance between surfaces of colliding particles/(2𝒗_𝟎)”, there is a chance that we had a few collisions where the particles were extremely close together, which resulted into a very small value of t_col. Hence, we could have a very large value of (1/t_col). Based on the 𝒗_𝟎 values reported above for the mentioned cells and that of 𝒗_𝟎^∗ under the conditions of study here, it is rational to only have one cell with a dark brown color in the “occupancy plot of collision frequency weighted volume of corrected agglomerating collision occurrence”.

## Slide 22: Conclusion
Developed an analytical energy balance model that accounts for the contributions of liquid capillary, viscous, and bridge volume effects, as well as the inelastic solid-solid collision.
The developed model offers the following advantages:
  Resolves mathematical issues presented in the original model proposed by Darabi et al. 2009 (Chem. Eng. Sci., 64, 1868-1876).
  Provides reasonable outcomes under both capillary and viscous limiting conditions with highly wetting systems.
  Introduced a computationally efficient evaluation algorithm to predict the collision outcome.
The model is useful for determining whether the collision dynamics are dominated by capillary or viscous effects, for sensitivity analysis, and for gauging operational risk.
The collision outcome was found to be sensitive to liquid layer thickness and asperity height (irregularity of particle shape), both of which evolve during the operation of the bed.
MFiX CFD-DEM simulations were used to provide particle collision information to the model.

## Slide 23
Jaber Shabanian (Jaber.Shabanian@Canada.ca)
Marc Duchesne (Marc.Duchesne@Canada.ca)
Allan Runstedtler (Allan.Runstedtler@Canada.ca)
Madhava Syamlal (Madhava.Syamlal@NETL.DOE.GOV)
Robin Hughes (Robin.Hughes@Canada.ca)
Thank you for your attention
Questions:

## Slide 24
Additional Slides

## Slide 25: Energy Balance Model
Stages during a binary identical wet particle collision:
Compare initial kinetic energy of particles with the total loss of energy that takes place during the collision interval between wet objects (here, two identical wet particles).
Approach: ()
Solid-solid contact: ()
Separation: ()

## Slide 26: Analytical Energy Balance Model
Compare initial kinetic energy of particles with approximate analytical values of energy losses due to the capillary and viscous effects as well as inelastic solid-solid contact during the collision interval between wet objects.
Equation of motion:
Numerical solution
Approximate analytical solution
Options to obtain energy losses
Neglect capillary effect
Loss of energy due to the capillary effect
Darabi et al., Chem. Eng. Sci. 64 (2009) 1868-1876.
For a binary collision of identical wet particles
Expressions for particle speed and losses of energy due to the viscous effect and inelastic solid-solid contact
Superposition principle
Approximate total loss of energy (maximum possible energy dissipation, ) during the collision

## Slide 27: Predict Collision Outcome by Darabi et al.’s Model
Darabi et al., Chem. Eng. Sci. 64 (2009) 1868-1876.
Determine the collision outcome based on the value of wet (overall) restitution coefficient ():
(elastic collision)
(completely inelastic collision)
(inelastic collision)
Collision outcome
(rebound)
(agglomeration)
!
!

## Slide 28: List of Assumptions
Colliding solid particles are spherical and identical in physical characteristics (e.g., size and height of asperities) and material.
Asperities have a negligible contribution to the total mass of a particle.
Particles are uniformly coated with a liquid layer.
Solid particles are coated with an identical amount of the same liquid.
The liquid bridge connecting the particles forms instantaneously, i.e., we neglect gas-film drainage effects that may prevent the coalescence of liquid coatings.
The liquid bridge volume remains constant during the collision interval.
The half-filling angle remains relatively unchanged with separation distance.
The height of liquid at the wetting radius, upon initial liquid contact, is the summation of the thickness of liquid layers from the colliding particles, i.e., for a binary collision of identical wet particles.
The tangential component of the viscous force is negligible.
Fluid flow fields around the colliding particles are identical.

## Slide 29: Darabi et al. vs. This Study (cont.)
Input parameters to evaluate the performances of the original and improved agglomeration models for two reference cases |  | 
 | Case I: water | Case II: hypothetical slag
Diameter of a solid particle, (µm) | 800 | 800
Particle density, (kg/m3) | 2650 | 2650
Dry restitution coefficient, (-) | 0.90 | 0.90
Height of a surface asperity, (µm) | 0.10 | 0.10
Thickness of the coating layer, (µm) | 5.00 | 0.15
Liquid viscosity, (Pa.s) | 8.9 × 10-4 | 10.0
Surface tension, (N/m) | 0.073 | 0.400
Contact angle, (deg) | 10 | 10
Input parameters to evaluate the performances of the original and improved agglomeration models for two reference cases |  | 
 | Case I: water | Case II: hypothetical slag
 | 800 | 800
 | 2650 | 2650
 | 0.90 | 0.90
 | 0.10 | 0.10
 | 5.00 | 0.15
 | 8.9 × 10-4 | 10.0
 | 0.073 | 0.400
 | 10 | 10
Base particle: silica sand
Binary collision of identical wet particles with identical impact speeds with respect to the frame in one dimension:
Darabi et al., Chem. Eng. Sci. 64 (2009) 1868-1876.
Darabi et al.’s agglomeration model
Models
This study’s agglomeration model
Shabanian et al., Chem. Eng. Sci. (2019) Submitted for publication.
For Darabi et al.’s model
For this study’s model

## Slide 30: Darabi et al. vs. This Study (cont.)
Darabi et al.’s model + speed conditions
This study’s model
Darabi et al.’s model
Hypothetical slag
Water
: critical particle speed

## Slide 31: Early Detection of Bed Defluidization
High Alarm: (HA)
Shabanian et al., Chem. Eng. J. 313 (2017) 144-156.
HA
HHA
Applicable to a Bubbling Gas-Solid Fluidized Bed
High-High Alarm: (HHA)
Shabanian et al., Powder Technol. 316 (2017) 139-147.
Defluidized bed

## Slide 32: Other Agglomeration Models for Wet Collisions
Generalized Analytical Energy Balance Model:
Equations of motion:
Viscous loss during the approach stage:
Force Balance Model:
Perform the evaluation in two steps:
1) Force balance at the point of solid-solid contact
2) Monitor particle velocities in the separation stage by the liquid bridge rupture distance

## Slide 33: Strategy
Coupled CFD-DEM modeling/simulation:
CFD: Gas as continuum phase; continuity & volume averaged Navier-Stokes equations
DEM: Particles as discrete phase; each particle is tracked in time and space by integrating the equations of motion
Advantages:
Provide detailed dynamic information about agglomeration phenomenon (e.g., particle trajectories & transient force exerting on individual particles) as DEM is a particle-level modeling tool.
Scrutinize the agglomeration phenomenon in all scales (micro, meso, and macro scales).
CFD governing equations:
DEM governing equations:
Xu & Yu, Chem. Eng. Sci. 52 (1997) 2785-2809.
Mansourpour et al., Chem. Eng. Res. Des. 92 (2014) 102-118.
Girardi et al., Chem. Eng. Sci. 144 (2016) 224-238.

## Slide 34: CFD-DEM for Primary Particles and Their Agglomerates
Governing equations for primary particles:
I
fcont
Governing equations for agglomerates:
Agglomeration criterion:
Kruggel-Emden et al., Powder Technol. 188 (2008) 153-165.
Mansourpour et al., Chem. Eng. Res. Des. 92 (2014) 102-118.
Rebound condition
Agglomeration condition
M
rcont
ri